        Acorn Computers Ltd - Science and Industry Division

        Technical Description and Service Manual

        Acorn Cambridge 32016 Co-Processor

Date of Issue: 2lst Jan. 86.

Issue: Issue 1.

Release History: Issue C - Fault finding/Test program.
        Issue B - 2nd Draft
        Issue A - Ist Draft

Reference No: 0410,000

  =================================================================

The product described in this manual and products for use with it,
are subject to a policy of continuous development and improvement.
All information of a technical nature and particulars of the product
and its use are given by ACORN Computers in good faith. However it is
acknowledged that there may be errors or omissions in this manual.

All maintenance and service on the product must be carried out by
ACORN Computers' authorised dealers. ACORN Computers can accept no
liability whatsoever for any loss or damage caused by service or
maintenance by unauthorised personnel.

This manual is intended only to assist the reader in the use of this
product, and therefore ACORN Computers shall not be liable for any
loss or damage whatsoever arising from the use of any information or
particulars in, or any omission in this manual, or any incorrect use
of the product.

Introduction ............................................. 2
     Nature and Purpose of the Manual .................... 2
     Sales Order Code .................................... 2
    Notation ............................................ 2
Mains power .............................................. 3
Hardware Technical Specfication .......................... 4
     Summary ............................................. 4
Packaging ................................................ 5
    Mechanical assembly of case ......................... 5
     Removing the lid .................................... 5
    Printed circuit - Removal ........................... 5
    Power supply - Removal .............................. 5
    General reassembly .................................. 6
Outline circuit description .............................. 7
    Main Components ..................................... 7
Detailed Circuit Description ............................ 10
    Clock scheme ....................................... 10
    Reset and Booting .................................. 11
Address map ............................................. 11
    Address map - during Booting ....................... 11
    Address map - after Booting ........................ 12
    Address decoding Logic ............................. 15
    RAS/CAS ............................................ 16
    Refresh ............................................ 16
    Interrupt .......................................... 16
Memory access cycles .................................... 17
    Memory access cycle without MMU .................... 17
     Row address (RAS Cycle) ............................ 17
    Column address (CAS Cycle) ......................... 17
    Read/write ......................................... 17
    Data validity ...................................... 18
    Memory access cycles with MMU ...................... 21
Links ................................................... 24
    Configuration ...................................... 24
Expansion instructions .................................. 24
    Memory ............................................. 24
    IMPORTANT NOTE ..................................... 24
    Memory manager ..................................... 24
Fault Finding ........................................... 25
    WARNINGS ........................................... 25
    Equipment Required. ................................ 25
    Fault Isolation .................................... 25
    Visual Check ....................................... 26
    Power Supply ....................................... 26
    Timing Signals ..................................... 26
    Processor Signals .................................. 27
    Boot (start-up) Sequence ........................... 27
    Tube Signals ....................................... 27
    Floating Point Faults .............................. 28
    Memory Faults ...................................... 28
Appendix A .............................................. 31
    Circuit Diagram .................................... 31
Appendix B .............................................. 32
    Memory Chip/Address Map ............................ 32
Appendix C .............................................. 33
    Oscilloscope Sync. Aid. ............................ 33
Appendix D .............................................. 34
     Available test software ............................ 34
Appendix E .............................................. 35
     Test program fault reports ......................... 35
Appendix F .............................................. 38
     Acorn Drawing Numbers .............................. 38

        Introduction

    Nature and Purpose of the Manual

The main purpose of this manual is to provide technical information
about the Acorn Cambridge 32016 Co-processor to the BBC Microcomputer
system.

The manual is aimed at technical service staff and includes an
outline technical specification and a detailed description of the
operation of the circuit. Information is also given about how to
upgrade the circuit and the purpose of the various links on the
board. Some guidance is also provided about fault-finding and
servicing.

    Sales order code

The Acorn Cambridge 32016 Co-processor has sales order code : ANCO5

    Notation

    ¦ = Active low signal (eg. ¦CAS)
    LSB = A0,D0 etc.
   MSB = A23,D15 etc.
   Word = two bytes = 16 bits
   Double = four bytes = 32 bits
   Quad = eight bytes = 6 bits
   NYA = Not yet available
   RSVD = Reserved for future (Acorn) use
   HHHHHH = Hex (Hexadecimal notation)
   BBBBBB = Bin (Binary notation)

References to IC numbers and signal names refer to issue 2 of Acorn
Drawing number 0110,000/C. A photo-reduced copy of which should be
attatched to this document. Where conflicts arise in the
documentation, the logic diagram should be assumed correct.

32016 Co-Processor 2 Technical Manual
        Mains power

WARNING: THE COMPUTER MUST BE EARTHED

IMPORTANT: The wires in the mains lead for the unit are coloured in
accordance with the following code:

GREEN & YELLOW - EARTH

BLUE - NEUTRAL

BROWN - LIVE

If the socket outlet available is not suitable for the plug supplied,
the plug should be cut off and the appropriate plug fitted and wired
as above. As the colours of the wires may not correspond with the
coloured markings identifying the terminals in your plug proceed as
follows:

The wire which is coloured green and yellow must be connected to the
terminal in the plug which is marked by the letter E, or by the
safety earth symbol, or coloured either green or green and yellow.

The wire which is coloured blue must be connected to the terminal
which is marked by the letter N, or coloured black.

The wire which is coloured brown must be connected to the terminal
which is marked by the letter L, or coloured red.

The moulded plug which was cut off must be disposed of carefully as
it would be a potential shock hazard if it were to be plugged in with
the cut off end of mains cord exposed.

The moulded plug must be used with the fuse and fuse carrier firmly
in place. The fuse carrier is of the same basic colour as the
coloured insert in the base of the plug. Different manufacturers
plugs and fuse carriers are not interchangeable.

In the event of the fuse blowing, it should be replaced, after
clearing any faults with a 3 amp fuse that is approved to 851362.

Do not use the unit in conditions of extreme heat, cold, humidity or
dust or in places subject to vibration. Do not block the ventilation
slots at the rear of the unit and ensure that no foreign objects are
inserted through any openings in the case.

32016 Co-Processor 3 Technical Manual
        Hardware Technical Specification

Acorn document No. 0310.000 is a formal specification for the 32016
Co-processor.

    Summary

The 32016 Co-processor is a "second processor" as described in the
BBC Microcomputer user guide.

The circuit is based around the National Semiconductors 32016 series
of processors and support devices which together provide a
performance comparable with modern mini-computers. The circuit has
been designed to allow operation at a processor clock rate of l0Mhz,
when using memory devices with a 150nS access time. The actual clock
rate will depend on the which National parts have been installed,
probably 6 Mhz. The socketed memory array can accept either 64K or
256K bit DRAMS and this allows the memory to be field upgraded to 1 M
Byte.

32016 Co-Processor 4 Technical Manual
        Packaging

The Acorn Cambridge 32016 Co-processor is supplied in a two Part
moulded polystyrene packing which is further packaged within a
cardboard sleeve. A mains lead and plug is packed with the 32016
Co-processor. The packaging should be kept intact in case it becomes
necessary to transport the unit at a later date.

        Mechanical assembly of case

    Removing the lid

WARNING: DO NOT REMOVE THE LID WITH THE MAINS POWER CONNECTED.

The lid of the Co-processor may be removed after undoing three fixing
screws, two on the rear panel and one underneath. When reassembling,
press the lid down at the rear whilst tightening the two rear fixing
screws. Take care not to lose the two spire clips pushed onto the
case lid, into which the rear fixing screws locate.

Inside the unit are two sub-assemblies, the power supply unit, and
main printed circuit board.

    Printed circuit - Removal

To remove the printed circuit board: remove the TUBE ribbon cable
from the socket on the printed circuit board and detatch the push on
power supply connectors; undo the six self-tapping screws that hold
the board to the case bottom and lift clear.

WARNING: THE PRINTED CIRCUIT BOARD CONTAINS DEVICES WHICH CAN BE
DAMAGED BY STATIC ELECTRICITY.

    Power Supply – Removal

To remove the power supply: detatch the mains live and neutral spade
connectors from the rear of the mains switch; remove the self-tapping
screw that secures the earth lead to the printed circuit board;
detatch the push on power supply connectors from the printed circuit
board; remove the six screws that hold the power supply to the bottom
of the case and lift clear. On reassembly ensure that the correct
screws are used.

32016 Co-Processor 5 Technical Manual
    General reassembly

To reassemble the Co-processor simply reverse the removal process.

CAUTION: BEFORE SWITCHING ON CHECK THE POLARITY OF THE 5V POWER
SUPPLY TO THE PRINTED CIRCUIT BOARD.

The output from the power supply is colour coded:

5V - RED

0V - BLACK

If in doubt check with a voltmeter before connection as reverse
polarity will destroy the components on the circuit board.

32016 Co-Processor 6 Technical Manual
        Outline circuit description

    Main Components

A block diagram of the circuit is shown in Fig.1.

A number of main component blocks can be identified, these are:

        Central processor unit (CPU) NS32016

        Memory Management unit (MMU) NS32082

        Timing and Control unit (TCU) NS32201

        Floating Point unit (FPU) NS32081

        Tube (R)

        Dynamic Memory array 64K/256K bit DRAMs

        EPROM 2 off 16K*8

The main bus connecting these components together is the AD bus, this
is a bidirectional multiplexed address/data bus.

The CPU is responsible for instruction fetch, decode, operand fetch
and the execution of integer arithmetic. Floating point instructions
together with the required operands are passed to the FPU for
execution.

If the system has an MMU installed, Virtual addresses generated by
the processor are intercepted by the MMU and mapped into Physical
addresses before being used to access the memory.

The TCU provides a number of system clocks at half the crystal
frequency. In addition it controls memory access cycles in
conjunction with some additional TTL based circuitry.

The TUBE (R) is a communications channel to the BBC Microcomputer
system which acts as host or I/O processor. Data passes through the
tube under program control0. An interrupt scheme is used on the 32016
side of the TUBE and polling is used on the Host side.

The socketed memory array is organised as two 1/4 M WORD sections.
Each section is further divided into low and high byte banks.

The Configuration links are read by software and indicate the
presence or absence of an FPU or MMU.

32016 Co-Processor 7 Technical Manual
The EPROMs contain PANDORA. This code is responsible for
initialisation on power-up and Break, and allows programs running on
the 32016 Co-processor access to the BBC operating system and
hardware. In practice all access to the BBC should be through PANOS,
the Acorn operating system for 32016 based products.

32016 Co-Processor 8 Technical Manual
        FIG.1. 32016 CO-PROCESSOR BLOCK DIAGRAM

        _______
        ¦ ¦
        AD0-23 ¦ ADDR. ¦ LA0-15
        _______________________________\_¦ ¦____\_
        ¦ ¦ / ¦ LATCH ¦ ¦
        ¦ Xtal. ¦ ¦ ¦ ¦
        ¦ ___¦___ ¦ ¦_______¦ ¦
        ¦ ¦ ¦ ¦ AD0-15 ¦
        ¦ ¦ TCU ¦ ¦ _______ ¦
        ¦ ¦_______¦ ¦ ¦ ¦ ¦
      ______ ¦ ¦ ¦ ¦ ¦ ¦
     ¦ ¦ ¦ ¦ ¦_/_____¦ EPROM ¦_/____¦
     ¦ ¦ ¦ _____ ¦ ¦ \ ¦ ¦ \ ¦
  ___¦ Tube ¦___¦ ¦ ¦ ¦ ¦ ¦_______¦ ¦
     ¦ ¦ ¦___¦ FPU ¦ ¦ ¦ ¦
     ¦______¦ ¦ ¦ ¦ ¦ ¦ _______ ¦
        ¦ ¦_____¦ ¦ ¦ ¦ ¦ ¦
To/From ¦ ¦ ¦ ¦ ¦ LA ¦
Host ¦ ¦ ¦ ¦ ¦ 8-15 ¦
        ¦ ¦ C ¦ ¦ DRAM ¦ ¦
        ¦ _____ ¦ L ¦_/_____¦ ¦_/____¦
        ¦ ¦ ¦ ¦ O \ ¦ ARRAY ¦ \ ¦
        ¦ ¦ ¦ ¦ C ¦ ¦ ¦
        ¦___¦ MMU ¦___¦ K ¦ ¦ ¦
        ¦ ¦ ¦ ¦ S ¦_______¦ ¦
        ¦ ¦ ¦ ¦ ¦ ¦ ¦
        ¦ ¦_____¦ ¦ ¦
        ¦ ¦ ______________________¦
    ________ ¦ ¦ LA1-7,16 ¦ ¦
   ¦ ¦ ¦ ¦ ¦ ¦
   ¦ ¦ ¦ _____ ¦ (CAS) ¦ _______ ¦
   ¦ Config.¦___¦ ¦ ¦ ¦ ¦ ¦ ¦ /¦\
   ¦ Links ¦ ¦ ¦ ¦ ¦ ¦_____\_¦ ¦ ¦
   ¦ ¦ ¦___¦ CPU ¦___¦ _______ / ¦ ¦ ¦
   ¦________¦ ¦ ¦ ¦ ¦ ¦ MUX ¦______¦
        ¦ ¦ ¦ ¦ ¦ ¦
        ¦_____¦ ¦ RFSH ¦_______\_¦ ¦ LA8-15
        ¦ COUNT ¦ / ¦ ¦
        ¦ ¦ ¦_______¦
        ¦_______¦

32016 Co-Processor 9 Technical Manual
        Detailed Circuit Description

Refer to the logic diagram where necessary.

    Clock scheme

The NS32201 Timing and Control unit produces a two phase MOS
compatable clock (PHI1 and PHI2). These are used internally by the
NS32OOO family only. For general use throughout the remainder of the
circuit the TCU provides CTTL which is a TTL compatable replica of
PHI1 clock. All the above mentioned clocks run at half the crystal
frequency. See Fig.2.

In order to reduce the probability of syncronisation failure occuring
the crystal oscillator input to the TCU is paused (low) if both the
host BBC Micro. and the 32016 access the tube simultaneously.

        FIG.2. CLOCK SCHEME

        ¦<------->¦
        ¦ ¦
        1/f
        ____ ____ ____ ____ ____
 XTAL ___¦ ¦____¦ ¦____¦ ¦____¦ ¦____¦ ¦____¦
 (At TCU)

        ->¦¦<-
        ¦¦ Delay through TCU
        ____ ____ ____ ____ ____
 FCLF ___¦ ¦____¦ ¦____¦ ¦____¦ ¦____¦ ¦____¦
        _________ _________ _________
 CTTL ___¦ ¦_________¦ ¦_________¦
        _________ _________ _________
 PHI1 ___¦ ¦_________¦ ¦_________¦
        ___ _________ _________
 PHI2 ¦_________¦ ¦_________¦ ¦_________

        ¦ 1/2f ¦
        ¦<----------------->¦

32016 Co-Processor 10 Technical Manual
    Reset and booting

Pressing BREAK on the keyboard causes a reset to occur in the host
processor, this causes ¦HRST on the host side of the Tube to go low
and this in turn causes ¦PRST on the 32016 side. ¦PRST is connected
to the TCU reset in (¦RSTI). The TCU produces a system reset (¦RSTO)
and it is this signal that resets the 32000 series devices.

During the reset recovery sequence (BOOTING) the CPU starts execution
at location Hex 000000 (Zero), however it also expects to find a
module table at location zero during program execution. This causes a
problem as this first instruction must be held in EPROM and the
module table must be in RAM. The problem has been solved using a
technique known as "RAM-FLIP". During BOOTING the address decoding
logic causes the EPROMs to appear at multiple locations including
zero and the RAM is disabled. The first instruction held in EPROM at
Hex 0000 is an unconditional branch into a high order copy of the
EPROM (Typically address Hex F00010). Execution continues with a
Write instruction (to no particular address) and this causes the
address decoding logic to switch out low order copies of the EPROMs
and enable the RAM.

The BOOTING sequence is controlled by an S-R latch formed by two
cross-coupled NAND gates (IC15). The output ¦BOOTING is set low by a
reset from the TUBE (¦PRST) and reset high by ¦WR. ¦BOOTING low
forces the EPROM chip select (¦ROMCS) active causing the EPROM to
respond to all addresses (ie it replicates at 16k word intervals)

        Address map

The address map is not fully decoded which means that some devices
(ie the TUBE) could be addressed at more than one location. The
address map is illustrated in Fig.3. Software must only access
devices at the addresses shown below.

    Address map - during Booting

See Fig.3.a

The EPROMs replicate from address Hex 000000 to Hex FFFFFF at 32k
byte intervals but are only addressed at:

        Hex 000000 (One instruction during start-up)
        and Hex F00000

32016 Co-Processor 11 Technical Manual

    Address map - after Booting

See Fig.3.b

After booting software must address:

        RAM Hex 000000 to Hex 0FFFFF

        EPROM Hex F00000

        Config. Switches Hex F90000

        TUBE TR1 Status Hex FFFFF0
        TR1 Data FFFFF2

        TR2 Status FFFFF4
        TR2 Data FFFFF6

        TR3 Status FFFFF8
        TR3 Data FFFFFA

        TR4 Status FFFFFC
        TR4 Data FFFFFE

32016 Co-Processor 12 Technical Manual
        FIG.3.a ADDRESS MAP DURING BOOTING

        ADDRESS (HEX)
        -------------

        ______________________________ Top: FFFFFF
        ¦ ¦
        ¦ EPROM (copy) ¦
        ¦______________________________¦
        ¦ ¦
        ¦ EPROM (copy) ¦
        ¦______________________________¦
        ¦ ¦

        ¦______________________________¦
        ¦ ¦
        ¦ EPROM (Pandora) ¦
        ¦______________________________¦ F00000
        ¦ ¦

        ¦______________________________¦
        ¦ ¦
        ¦ EPROM (copy) ¦
        ¦______________________________¦
        ¦ ¦
        ¦ EPROM (Vector into Pandora) ¦
        ¦______________________________¦ Bottom: 000000

Note: The EPROMs replicate in memory during booting.

32016 Co-Processor 13 Technical Manual
        FIG.3.b ADDRESS MAP AFTER BOOTING

        ADDRESS (HEX)
        -------------

        ______________________________ Top: FFFFFF
        ¦ ¦
        ¦ TUBE ¦
        ¦______________________________¦ FFFFF0-FFFFFE
        ¦ ¦

        ¦______________________________¦
        ¦ ¦
        ¦ Config. Switches ¦
        ¦______________________________¦ F90000
        ¦ ¦

        ¦______________________________¦
        ¦ ¦
        ¦ EPROM (Pandora) ¦
        ¦______________________________¦ F00000
        ¦ ¦

        ¦______________________________¦
        ¦ ¦
        ¦ ¦
        ¦ RAM ¦
        ¦ ¦
        ¦ ¦
        ¦______________________________¦ Bottom: 000000

Note: The address decoding may not be as "tight" as indicated

      in this diagram.

32016 Co-Processor 14 Technical Manual
    Address decoding logic

Multiplexed addresses from the processor or memory manager on
AD0-AD15 are latched into IC23 and IC24 and remain stable throught a
bus cycle. Address lines A16 to A23 do not require latching as they
are not multiplexed.

A23 is used to enable/disable ¦CAS to the memory chips preventing
access outside the bottom 4 M bytes (ie when reading other devices).

Address decoding within the 1 M byte is performed by allowing ¦CAS to
selected banks only. This is performed by IC28 (address bit A17 )
according to the following table.

With 64k (256k) bit DRAMS installed:

        A17 (A19) ¦CAS Enables
        --------- ------------

        0 Low 1/8th (1/2) M byte

        1 Hi 1/8th (1/2) M byte

High Byte Enable (¦HBE) is used together with A0 to enable low and
high byte banks according to the following categories ( Note: A word
located at an ODD address requires two memory cycles ).

       Category ¦HBE A0 ¦CAS's enabled
        -------- ---- -- --------------

       Even Byte 1 0 Low byte enabled
      Odd Byte 0 1 High byte enabled
      Even Word 0 0 Both bytes enabled

       Odd Word:
        Odd Byte 0 1 High byte enabled
        Followed by
        Even Byte 1 0 Low byte enabled

Other categories for Even/Odd Double Word and Quad accesses exist but
are simply a repetition of two or more of the above. For more
information see NS data sheets for the 32016.

¦RAS plays no part in the address decoding scheme and all RAM devices
are RASed on every access. Note this has no effect on the RAMs other
than causing the addressed location to be refreshed.

The top 1 M byte is loosely decoded by IC14 to provide chip select
signals for the tube (¦TUBE), The configuration links (¦CONFIG), and

32016 Co-Processor 15 Technical Manual
the EPROM (¦HPROM). See the previous section on the address map for
the correct addresses.

    RAS/CAS

One half of the mulitiplexer (IC25/26) is used to supply column
addresses to the DRAMS on Latched Address lines LA8-15. Line
termination resistors (33 Ohms) are used to reduce reflections on the
address lines caused by the high capacitance of the Drams and long
length of these tracks. The 9th row and column address bit required
by 256k bit DRAMS is provided by IC19 and is A18 during RAS and A17
during CAS.

    Refresh

Refresh is performed by inserting wait states into the memory cycle,
enabling the refresh address counter (IC27) onto the bus and giving
RAS (Known as "RAS only" refresh). IC7 is a binary counter which
counts CTTL cycles and generates a refresh cycle every l6uS
(approximatly). The HAS timing for this cycle is provided by the
sequencer/shift-register based around IC12 and IC13. If a memory
cycle is in progress when the refresh access starts it is delayed by
¦CWAIT and restarted when the refresh cycle ends.

    Interrupts

The only source of interrupts is the TUBE so there was no need to use
an Interrupt Control Unit (ICU NS32202) in this design.

Additional protection against synchronisation failure is provided by
latching ¦PIRQ and ¦PNMI on the rising edge of CTTL in IC5 before
feeding the interrupts to the processor.

IC6 is a programable device which implements a simple state machine
and is used to prevent interrupts from occuring during and just after
certain instruction sequences. This device is only necessary when
some revisions of the Memory Manager are used and is bypassed by
links LK CNM and LK CIR when not fitted.

32016 Co-Processor 16 Technical Manual
Memor access les

Memor access le without MMU

Non memory managed bus cycles are shown in fig. .a

A memory cycle is initiated by the processor putting an address on
the AD bus and pulling ADdress Strobe (|ADS) low. While |ADS is low
the address de-multiplexing latch (IC23,2 -LS373) is transparent and
the Row address is passed through to the DRAMS. When |ADS returns
high the address is held in the de-multiplexing latch.

Note: It is not necessary to latch the top eight address bits as they
remain valid during the entire bus cycle.

 Row address (BAS Cy le)

While IRAs is false (HI) the RAS driver bank is enabled and the upper
9 bits are supplied to the DRAMS. In response to |ADS going low the
TCU after one cycle generates |TSO. This in turn causes IRAs (DRAM
pin ) to go low and the row address is strobed into the DRAMS.

 Column address (CAS Cycle)

|TSO going low removes the row address from the LA8-15 by making IC2
tristate, and enables the column address via multiplexer IC25 and
IC26. |TSO low releases the|CL -Clear input of ICll and allows the
next CTTL edge to generate |CAS and The Column address is strobed
into the DRAMS.

The direction of the memory access (Read or Write) is signaled to the
TCU by Data Direction In (|DDIN) and it is the TCU that generates
READ ([RD) or WRITE (|WR) accordingly. |WR is distributed to all
DRAMS, and |RD is used to enable the TURK and EPROM.
32016 Co-Processor
17
Technical Manual
During a read cycle the processor expects the data returned from
memory to be valid before the end of PHI2 during |TSO low.

During a write cycle the processor provides valid data during |WR
low.
32016 Co-Processor
18
Technical Manual
FIG.4.8. . NON MEMORY MAN ED BUS CYCLE

 CPU BUS SIGNALS

| Tl | T2 | T3 | T4 |
Phi I
Phi 2
----_
I I I I I E I I t
        I I t t t t t t t
-----
I 1 I I I t { I I
I I t I I I t I I

---_-
E I I I I I I I I
        t I I I I t I I I
AD16-23 / addr \__
\ /
ADO-15
(Read)
  | addr \ / data| \_/
\ / \ | / \_
{
I
Read data sampled by CPU

ADO-15 / addr \/ data \_
(Write) \ /\ /
~
\ /
| ADS
- _
\| \/
 /\ /\_
| HER
-
32016 Co-Processor
19
Technical Manual
| RD

 or
  |WR
 | DBE

|TSO
I I , I I
{ , , f I

\ /
\ |
32016 Co-Processor
20
Technical Manual
 Memory access cles with MMU.

Memory managed cycles are shown in fig. .b

In this case the processor places a VIRTUAL address on the AD bus and
]ADS from the processor is used to strobe the address into the MMU.
The MMU uses an internal translation table to "look-up" the
coresponding PHYSICAL address which it places on the AD bus one cycle
later. |PAV from the MMU looks to the TCU like |ADS from the
processor and the memory access then continues in the same way as the
non-memory managed case but one cycle late.

The memory manager maintains its internal translation table (Cache)
without intervention from the processor. If the table entry required
is not held in the MMU it is fetched from the larger page table in
main memory. In this case the CPU memory cycle is paused while the
MMU updates its table entry using a normal memory access cycle. If
the MMU detects an illegal access or an access to an address which
does not reside in RAM a trap will occur and the trap handling
mechanism of the 32016 will be invoked. For a more detailed
description of the MMU and its function refer to NS32082 data sheets.
32016 Co-Processor
21
Technical Manual
 FIG.4.b. MEMORY MANAGED BUS CYCLE
 CPU BUS SIGNALS
| Tl | TMMU | T2 | T3 | T4 |
__---
I I I I I [ } I I I [
I [ I I I I I I I I I

___---
I I I I I I I I I I I
[ I I [ I I I I I I I
-----
 fl I | | | I I I | I I
Phi I
Phi 2
AD16-23 / Virtual I/ Physical I__
I,Addr /I_Addr /
ADO-1
(Read)
  \ Virtual \/ Physical\ / data I I
I__Addr /I__Addr / \ | /
I
I
Read data sampled by CPU
ADO-15 / Virtual I/ PhyscalI/ data I__
(Write) \_Addr /\_Addr /\ /
|ADS
(CPU)

|PAV
(MMU)

|ADS
(TCU)
-
\ /
       , .. write
|DDIN \/ \/
    /\ read /\___
| HBE
32016 Co-Processor
22
Technical Manual
 TCU BUS SGNALS

I I
I I
| RD
or
| DBE

|TSO
32016 Co-Processor
23
Technical Manual
Links
These are read by software on power-up and indicate the presence OT
absence of optional hardware (ie FPU or MMU). The links have one side
connected to OV the other side is pulled high by resistors and can be
read onto the AD bus through IC3O. A link to OV indicates :
H
G
F
E
No FPU
No MMU
RSVP
RSVD
D
C
B
A
RSVP
RSVD
RSVP
RSVD
 Memory
The printed circuit board has a total memory capacity of 1 M Byte and
can be upgraded to this total by adding using a 12k memory upgrade
kit. Acorn Product Code AND 26.

The memory upgrade kit contains sixteen 2 6k bit DRAMS which have to
be inserted into the empty sockets in the memory array.
 IMPORTANT NOTE
It is strongly advised that DRAMS from different manufacturers arc
NOT mixed within the same 1 M byte bank. For this reason the upgrade
kits will be marked externally with the manufacturers name, and this
should be specified when ordering upgrade kits when ever possible.
Memo ana er
NYA
32016 Co-Processor
Technical Manual
 WARNINGS
Before starting it should be realised that any attempt at repair by
any person other than a registered dealer or service agent will void
the warranty.

Be extremely careful when extracting the 32016 Processor from its
socket, it is all too easy to crack the ceramic package and destroy
the device which is expensive.

It is assumed that you have available the circuit diagram of the
unit, normally distributed with this document.

 Equipment Required.

The following is a list of equipment needed to diagnose faults in the
32016 hardware.

(a) U.K. BBC Micro Model B (with disc interface).
Cb) An 80 track single disc drive.
Cc) Colour/Monochrome monitor.

The minimum test equipment needed in order to trace a fault is a
digital multimeter and an oscilloscope. The oscilloscope should have
at least two traces and two timebases, and should have a bandwidth of
around 5OMHz or higher. Other useful pieces of 'test equipment' are:
A can of freezer spray; a hair dryer (or commercial hot air blower);
a selection of IC test clips (ie Radio Spares 23-627 and 2 -018).
Unless you have a good idea about where the fault is it is probably
best to follow a definite order in testing the unit. To start with
there are a number of simple tests which you can use to establish
whether the 32016 hardware is working at all.
32016 Co-Processor
25
Technical Manual
 Visual Chck
First perform a visual inspection of the interior of the Coprocessor,
check that all external connections ( TUBE ribbon cable and the mains
lead) are secure and in good condition. Check that no foreign objects
(washers etc.) have found their way into the case. Also check that
the EPROMs and Molex links are inserted correctly.
 Power Suppl
Make sure that power is getting to the 32016 board from the on board
power supply unit. This means checking for the presence of the +5V
supply line and also that the connection to the board is good, the
best course of action is to put the DMM across the Faston connectors
and check for five volts. You should also check that the PSU is
connected to the CPU board the right way round. The tabs are marked
OV and +5V so this is just a matter of checking that the red wire is
connected to the positive (+5V) tab.
Timi als
NOTE: The program found in appendix C will be invaluable as an aid to
fault finding when using an oscilloscope.

CLOCKS: Check for the presence of the clock signals XCTLI, PHII. PHI2
and CTTL (pins 13, 11. 10 and 16 on the TCU). These may be checked
against the Fig.2. The TCU generates all system clocks from the
double frequency crystal XCTL (FCLK is a buffered version of XCTL).
The two clocks PHII and PHI2 should have rising edges on alternate
rising edges of FCLK. CTTL is just a TTL compatible version of PHII.
Check that these key clock signals arrive at the CPU and FPU where
appropriate.
RESET: Check that the system reset is functional by
sequence of events described in the preceeding text as
alternatly pressing and releasing the break key check
on:
HRST - Host Reset - Pin 20, ICl
PRST - Parasite Reset - Pin 37. ICl
RSTI - Reset in (TCU) - Pin 7, IC32
RSTO - Reset out (TCU) - Pin 8, IC32
RSTO - " - Pin 3 , IC31
RSTO - " - Pin 1 , IC2
following the
follows. While
for activity
All these signals should go low and rise again when the BREAK key is
released.
32016 Co-Processor
26
Technical Manual
 Processor Signa
]ADS: The lower sixteen lines of the bus are multiplexed address/data
lines. The address strobe line, ADS, goes low for approx. a half
cycle of PHII at the beginning of each bus cycle - indicating a valid
address is present on AO-Al . For example when the CPU is executing
reads there will be a pulse on ADS (pin 6 of the TCU) approximatly
every four clock cycles. The activity on the ADS pin should be
checked for as it indicates that the CPU is attempting to access the
outside world and is not be completly dead.

]DDIN: This indicates to the TCU the direction of data on the data
bus (ie low indicates data in - read, hi indicates data out - write).
Check for activity on this pin. In response to ]DDIN the TCU
generates Read - ]RD Pin 3, Ic4 and Write - |WR Pin 4, Ic4. Check for
activity on these pins.

]PPS: Program Flow Status. This pin (active low) gives a pulse
every time a new instruction begins execution. A stream of pulses
on PPS (pin 39) is a good indication that the processor is executing
instructions.

|IRQ: The maskable interrupt 1 n is used whenever information is
passed down the tube. It is a bit difficult to get this line active
during testing unless you have special test software to run on the
32016 and the machine is in a fit state to run it. Check that ]INT
and ]NMI are not stuck low.

The Boot sequence is described in the proceeding text. Having checked
that the reset system is operational it is worth examining the signal
"BOOTING" which can be found on Pin 6, Icl . This signal is low for a
very short period after reset ( one or two instructions) and then
remains high until the next reset. If this signal is correct it
indicates that the processor is able to fetch and execute the first
few instructions in the EPROM, and usually the fault is elsewhere.
 Tube Si als
After reset the processor should output a message similar to:

PANDORA 32016 version X.XX
Memory size = ..... etc

This message is passed through the TUBE by the processor. While this
message is being transfered there should be activity on the TUBE chiP
select Pin 21, ICl. If this message is displayed there is a good
chance that the tube is functioning correctly.
32016 Co-Processor
27
Technical Manual
 Floating Point Faults

If the floating point chip is faulty it will usually show up in one
of two ways: It will either not respond when asked to perform
floating point arithmetic, or will (more rarely) give the wrong
answer.

In the first case the Coprocessor may appear dead because PANDORA
checks for the presence of an FPU if the configuration links say
there should be one. A quick test would be to remove the FPU
configureation link and press BREAK. If the Coprocessor now works the
FPU is at Fault.

The second case is difficult to diagnose as the symptoms can appear
unrelated to the FPU. The best method of identifying this type of
fault it by replacing the suspect FPU with a known good device.

The FPU test supplied with some versions of the Memory test program
is very simple and unlikley to detect faults of the second kind.
 Memory Faults
Most common faults will be concerned with memory and/or the incorrect
instalation of memory upgrade kits. To aid fault finding an EPROM or
80 TRACK DISC based memory test program is available to authorised
dealers and production sites (ACORN Product Code ??????). This
program is designed to help quickly identify faults in the memory
system, and can be used to check that memory upgrades have been
installed correctly.

The symptoms of memory failure are varied and include:

1) Pandora's start-up message incorrectly states the memory size.
2) Some small programs will run but not other larger ones.
3) A program will not run with an editor loaded.
4) Random corruption of files loaded into memory.

The disc based version can be run by inserting the disc in the drive
and pressing SHIFT+D while pressing and releasing BREAK. ( A Boot
file is provided). The disc version requires some memory itself and
so is only useful for testing the memory of an assembled AC .

The program is also available on two EPROMs which are temporarily
inserted in place of the two Pandora EPROMs installed during
manufacture. This must be done with the power to the unit switched
off or disconnected, and with some care as damage may result from
incorrect insertion.

The program writes a fixed pattern into memory and then reads it back
checking each word in turn. The pattern written into memory is cycled
Hex 21 times because memory faults are often "pattern-sensitive".
(This is the main reason that all memory test programs take a long
time to run, in this case approximatly mins to test 1 Mbyte.
Proportionaly less for smaller machines).

On start-up a menu similar to FIG.5. should be displayed.

You should then press a key between O and 7 according to the size of
memory installed. Eg. press "2" for 1.5 M byte produces.

Select: Testing 1.5 M Bytes
Cycle - XX
The "Cycle - XX" message gives an indication of how far the test
program has got. The test takes Hex 21 cycles. If a mistake is made
in selecting the memory size, then it is quite in order to press
BREAK and re-start the program.

Examples of various faults and their corresponding error reports are
given in appendix E.
32016 Co-Processor
29
Technical Manual
 Pi g . 5 TEST PROGRAM M
Key

O
1
2
3
LI

5
6

7
8

9
Select:
M bytes)

bytes)

M bytes)

bytes)

M bytes)

bytes)

M bytes)

bytes )
Test
Walking 16 bit memory test (0.5
Walking 16 bit memory test (1 M

Walking 16 bit memory test CI.5

Walking 16 bit memory test (2 M
Walking 16 bit memory test (2.5

Walking 16 bit memory test (3 M

Walking 16 bit memory test (3.5

Walking 16 bit memory test ( M

Refresh test

Floating Point Unit (FPU) test
32016 Co-Processor
30
Technical Manual
 Appendix
The circuit diagram has ACORN drawing number 0110,0O0/C
32016 Co-Processor
31
Technical Manual
 Appendix_

Memorv Chin/Address Man

lssue 2 printed circuit board:
High byte
-~~------
Low byte
--------
Dl5...................D8 D7...................DO

00000 . . . 7FFFF 37 38 39 !10 !ti /12 !13 !t!1 29 30 31 32 33 3~ 35 36
80000...FFFFF 53 5 55 56 57 58 59 60 5 6 !17 8 9 50 51 52
32016 Co-Processor
32
Technical Manual
 Appendix_C

 Oscilloscope_S nc id.
The bus activity during execution of any program (incl. Pandora) will
be very random and difficult or impossible to follow with an
oscilloscope. The following program when run in the BBC Micro. resets
the Coprocessor at a few hundred Hertz. This causes the Coprocessor
to repeat the start up sequence rapidly, and provides a triggering
mechanisim for an oscilloscope.

The program is written in BBC BASIC.

10 ?&FEEO = &7F
20 REPEAT ?&FEEO = &AO : ?&FEEO = &20 : UNTIL O
This should be entered as follows.

i) Turn off the Coprocessor.
2) Press BREAK.

3) Enter the program above exactly as shown.

4) RUN the program.

v) Turn on the Coprocessor again.
The 32016 is now reseting about 500 times a second. Note that nothing
will be displayed on the screen to indicate this.

It is now possible to follow the start Up sequence triggering the
oscilloscope on the RISING edge of one of the reset signals ie.
jRSTO. First look for this signal on the reset pin of the CPU (pin
3).
]Et Will not be possible to obtain a perfectly stable signal because
for various reasons the BBC 6502 does not always execute line 20 in
the same amount of time, and the execution of the start-up sequence
in the 32016 is disturbed by memory refresh cycles.
32016 Co-Processor
33
Technical Manual
 Appendix D

 Available test sotwar
Title
Media Code
32016 Memory test/EPROM EPROM/ROM Low 2201,229
High 2201.230
32016 Co-Processor
Technical Manual
A eppix E
 Test pro am fault reports

Any faults reported take the following format:

Error addr: HHHHHH - This is the hex address of the fault.

Written: BBBBBBBB BBBBBBBB - This is the binary data written
into memory at the faulty address
(Dl5...D8 D7...DO).

Read: BBBBBBBB BBBBBBBB - This is the binary data read back from
the faulty address (Dl5...D8 D7...DO).

Some examples will illustrate how this information can be used to
identify a variety of faults. See Fig.6.

Example 1.- A faulty DRAM

In this example bit D5 is "stuck-at-1" but only at a small number of
addresses. To find out which DRAM contains this bit at this address
use the tables in Appendix B. In this example the fault is in IC52.

Example 2. - Faulty PCB (Data bit) or faulty DRAM

At first glance this looks similar to example one but note that ALL
addresses are failing one bit, this could indicate a faulty DRAM, a
DRAM in the wrong way around, or a fault on the PCB (ie a short
circuit ).

Example 3. - Faulty PCB (Address bit)

Because each memory bank has its own set of address buffers a faulty
address line may not show up as a fault at all addresses. A typical
fault report is shown, note that the pattern read from the memory
appears correct but shifted up or down in memory. It is impossible to
write a test program that will fully identify faults of this kind
which may be caused by an address line shorted to any other signal or
power/ground.

Example . - Refresh fault

If a random or semi-random pattern is read from the memory, you
should suspect a fault in the refresh circuitry. The act of writing
or reading refreshes the dynamic memory so this is unlikley to be the
cause of a fault reported while testing small amoumts of memory (ie.
1/2 M byte). A refresh test program option is provided.
32016 Co-Processor
Technical Manual
3 5
FIG.El. MEMORY TEST PROGRAM FAULT EXAMPLES

a/. Faulty DRAM
Error addr: 0000878 Written: 11111111
Error addr: OOOO8BB Written: 10111111
Error addr: 0000978 Written: 00000000
Error addr: oOooABB~ Written: 11011111
Error addr: OOOOCBB Written: 11101111
Error addr: OOOOD7B Written: 11111111
Error addr: OOOOEBB Written: 11110111

b/. Faulty PCB (Bit D9) or DRAM
Error
Error
Error
Error
Error
Error
Error
Error
Error
Error
Error
Error
addr:
addr:
addr:
addr:
addr:
addr:
addr:
addr:
addr:
addr:
addr:
addr:
00000000
00000002
0000000
00000006
o0o000o8
OOOOOOOA
OOOOOOOc
OOOOOOOE
00000010
00000012
0000001
00000016
Written:
Written:
Written:
Written:
Written:
Written:
Written:
Written:
Written:
Written:
Written:
Written:
00000000
10000000
01000000
00100000
00010000
00001000
00000100
00000010
00000001
00000000
00000000
00000000

00000000
00000000
00000000
00000000
00000000
00000000
00000000
00000000
00000000
11111111
01111111
00111111
11111101
11111111
00000001
11111111
11110111
11111111
11111111

1
I

00000000
00000000
00000000
00000000
00000000
00000000
00000000
00000000
00000000
10000000
01000000
00100000

10000000
01000000
00100000
00010000
00001000
00000100
00000010
00000001
00000000
11111111
11111111
11111111
Read:
Read:
Read:
Read:
Read:
Read:
Read:
Read:
Read:
Read:
Read:
Read:
Read:
Read:
Read:
Read:
Read:
Read:
Read:

Read:
Read;
Read:
Read:
Read:
Read:
Read:
Read:
Read:
Read:
Read:
Read:
11111111 11111100
10111111 11111110
00000000 00000000
11011111 11111110
11101111 11111110
11111111 11111110
11110111 11111110

I
I

Stuck bit
00000010 00000000
10000010 00000000
01000010 00000000
00100010 00000000
00010010 00000000
00001010 00000000
00000110 00000000
00000010 00000000
00000011 00000000
00000010 10000000
00000010 01000000
00000010 00100000
Stuck bit
c/. Faulty address line
Error
Error
Error
Error
Error
Error
Error
Error
Error
Error
Error
Error
addr:
addr;
addr:
addr:
addr:
addr:
addr:
addr:
addr:
addr:
addr:
addr:
00000000
00000002
0000000
00000006
00000008
OOOOOOOA
OOOOOOOc
OOOOOOOE
00000010
00000012
0000001
00000016
Written:
Written;
Written:
Written:
Written:
Written:
Written:
Written:
Written:
Written:
Written:
Written:
00000000
00000000
00000000
00000000
00000000
11111111
01111111
10111111
11011111
11101111
11110111
11111011
00010000
00001000
00000100
00000010
00000000
11111111
11111111
11111111
11111111
11111111
11111111
11111111
Pattern shifted up/down
32016 Co-Processor
36
Technical Manual
FIG. El . MEMORY TEST FROG AULT EXAMPLES CQNT.

d/. Refresh fault
Error
Error
Error
Error
Error
Error
Error
Error
Error
Error
Error
addr:
addr:
addr:
addr:
addr:
addr:
addr:
addr:
addr:
addr:
addr:
00000002
QQQQQQQ
QQQOQQQ6
QQQQQQQ8
QQQQQQQA
OQQOOOQC
QQQQQQQE
QQQQQQIQ
QQQQQQ12
QQQQQQI
QQQQQQ16
Written:
Written:
Written:
Written:
Written:
Written:
Written:
Written:
Written:
Written:
Written:
01000000
QQIQQQQQ
QQQIQQQQ
QOQQIQQQ
OQQQQIQQ
OOOQQQIQ
QOQQQQQI
QQQQQQQQ
QQQQQQQQ
QQQQQQQQ
QQQQQQQQ
00000000
QQQQQQQQ
QQQQQQQQ
QQQQQQQQ
QQQQQQQO
QQQQQOOO
QQQQQQQO
IQQQQQQQ
QIQQQQQQ
QQIQQQQQ
QQQIQQQQ
Read:
Read:
Read:
Read:
Read:
Read:
Read:
Read:
Read:
Read:
Read:
00000000
IlQQlQQl
OQIQIQIO
OQIQIQQO
OQIQIQIO
QlQllQll
IOOlQlQl
QQQQQIQQ
IIQQQQQQ
IQQQIQQI
IlQllQll
00001000
IQQIQQIQ
QlQQllQl
IllQQQlO
IlQQlQlO
QllQllOl
OIQIQQIO
IlQlllll
QQQQQIII
QQIQQIQI
IllQQlll
32016 Co-Processor
37
Technical Manual
A eix F

 Acorn Drawin N ers

Acorn Cambridge 32016 Co-Processor Specification
0310,000
Acorn Cambridge 32016 Co-Processor Technical Description
and Service Manual 0 10,000

Acorn Cambridge 32016 Co-Processor Circuit Diagranl 0110,000/C
32016 Co-Processor
38
Technical Manual