Acorn iEEE488 Interface

# IEEE-488 Bus Overview
## Bus history
The IEEE-488 bus was developed to connect and control programmable instruments, and to provide a standard interface for communication between instruments from different sources. Hewlett-Packard originally developed the interfacing technique, and called it HP-IB. The interface quickly gained popularity in the computer industry. Because the interface was so versatile, the IEEE committee renamed it GPIB (General Purpose interface Bus).
## IEEE-488 overview
Almost any instrument can be used with the IEEE-488 specification, because it says nothing about the function of the instrument itself, or about the form of the instrument's data. Instead the specification defines a separate component, the interface, that can be added to the instrument. The signals passing into the interface from the IEEE-488 bus and from the instrument are defined in the standard. The instrument does not have complete control over the interface. Often the bus controller tells the interface what to do. The Active Controller performs the bus control functions for all the bus instruments.
## System controllers and the active controller
At power-up time, the IEEE-488 interface that is programmed to be the System Controller becomes the Active Controller in charge. The System Controller has several unique capabilities including the ability to send Interface Clear (IFC) and Remote Enable (REN) commands. IFC clears all device interfaces and returns control to the System Controller. REN allows devices to respond to bus data once they are addressed to listen. The System Controller may optionally Pass Control to another controller, which then becomes Active Controller.
## Listeners, talkers and controllers
There are 3 types of devices that can be connected to the IEEE-488 bus (Listeners, Talkers, and Controllers). Some devices include more than one of these functions. The standard allows a maximum of 15 devices to be connected on the same bus. A minimum system consists of one Controller and one Talker or Listener device (i.e., an Acorn BBC with an IEEE-488 interface and a voltmeter).
It is possible to have several Controllers on the bus but only one may be active at any given time. The Active Controller may pass control to another controller which in turn can pass it back or on to another controller. A Listener is a device that can receive data from the bus when instructed by the controller and a Talker transmits data on to the bus when instructed. The Controller can set up a talker and a group of listeners so that it is possible to send data between groups of devices as well. Most controllers have talker and listener capabilities as well.
## Interface signals
The IEEE-488 interface system consists of 16 signal lines and 8 ground lines. The 16 signal lines are divided into 3 groups (8 data lines, 3 handshake lines, and 5 interface management lines).
## Data lines
The lines DIO1 through DIO8 are used to transfer addresses, control information and data. The formats for addresses and control bytes are defined by the IEEE 488 standard. Data formats are undefined and may be ASCII (with or without parity) or binary. DIO1 is the Least Significant Bit (note that this will correspond to bit 0 on most computers).
## Handshake lines
The three handshake lines (NRFD, NDAC, DAV) control the transfer of message bytes among the devices and form the method for acknowledging the transfer of data. This handshaking process guarantees that the bytes on the data lines are sent and received without any transmission errors and is one of the unique features of the IEEE-488 bus.
The NRFD (Not Ready for Data) handshake line is asserted by a Listener to indicate it is not yet ready for the next data or control byte. Note that the Controller will not see NRFD released (i.e., ready for data) until all devices have released it.
The NDAC (Not Data Accepted) handshake line is asserted by a Listener to indicate it has not yet accepted the data or control byte on the data lines. Note that the Controller will not see NDAC released (i.e., data accepted) until all devices have released it.
The DAV (Data Valid) handshake line is asserted by the Talker to indicate that a data or control byte has been placed on the data lines and has had the minimum specified stabilizing time. The byte can now be safely accepted by the devices.
## Handshaking
The handshaking process is outlined as follows. When the Controller or a Talker wishes to transmit data on the bus, it sets the DAV line high (data not valid), and checks to see that the NRFD and NDAC lines are both low, and then it puts the data on the data lines.
When all the devices that can receive the data are ready, each releases its NRFD (not ready for data) line. When the last receiver releases NRFD, and it goes high, the Controller or Talker takes DAV low indicating that valid data is now on the bus.
In response each receiver takes NRFD low again to indicate it is busy and releases NDAC (not data accepted) when it has received the data. When the last receiver has accepted the data, NDAC will go high and the Controller or Talker can set DAV high again to transmit the next byte of data.
Note that if after setting the DAV line high, the Controller or Talker senses that both NRFD and NDAC are high, an error will occur. Also if any device fails to perform its part of the handshake and releases either NDAC or NRFD, data cannot be transmitted over the bus. Eventually a timeout error will be generated.
The speed of the data transfer is controlled by the response of the slowest device on the bus, for this reason it is difficult to estimate data transfer rates on the IEEE-488 bus as they are always device dependent.
## Interface management lines
The five interface management lines (ATN, EOI, IFC, REN, SRQ) manage the flow of control and data bytes across the interface.
The ATN (Attention) signal is asserted by the Controller to indicate that it is placing an address or control byte on the data bus. ATN is released to allow the assigned Talker to place status or data on the data bus. The Controller regains control by reasserting ATN; this is normally done synchronously with the handshake to avoid confusion between control and data bytes.
The EOI (End or Identify) signal has two uses. A Talker may assert EOI simultaneously with the last byte of data to indicate end-of-data. The Controller may assert EOI along with ATN to initiate a parallel poll. Although many devices do not use parallel poll, all devices should use EOI to end transfers (many currently available ones do not).
The IFC (Interface Clear) signal is asserted only by the System Controller in order to initialize all device interfaces to a known state. After releasing IFC, the System Controller is the Active Controller.
The REN (Remote Enable) signal is asserted only by the System Controller. Its assertion does not place devices into remote control mode; REN only enables a device to go into remote mode when addressed to listen. When in remote mode, a device should ignore its local front panel controls.
The SRQ (Service Request) line is like an interrupt: it may be asserted by any device to request the Controller to take some action. The Controller must determine which device is asserting SRQ by conducting a serial poll. The requesting device releases SRQ when it is polled.
## Device addresses
The IEEE-488 standard allows up to 15 devices to be interconnected on one bus. Each device is assigned a unique primary address, ranging from 0-30, by setting the address switches on the device. A secondary address may also be specified,ranging from 0-30. See the device documentation for more information on how to set the device primary and optional secondary address.
## Physical characteristics
You can link devices in either a linear, star or combination configuration using a shielded 24-conductor cable. The standard IEEE-488 cable has both a plug and receptacle connector on both ends. This connector is the Amphenol CHAMP or Cinch Series 57 MICRO RIBBON type. Special adapters and non-standard cables are available for special interconnect applications.
The IEEE-488 bus specifies a maximum total cable length of 20 meters with no more than 20 devices connected to the bus and at least two-thirds of the devices powered on. A maximum separation of 4 meters between devices and an average separation of 2 meters over the full bus should be followed. Bus extenders and expanders are available to overcome these system limits.
The bus uses standard TTL level negative logic. When NRFD is true for example it is a TTL low level, and when NRFD is false, it is a TTL high level.
## Summary
The IEEE-488.1 standard greatly simplified the interconnection of programmable instruments by clearly defining mechanical, hardware, and electrical protocol specifications. For the first time, instruments from different manufactures were connected by a standard cable. This standard does not address data formats, status reporting, message exchange protocol, common configuration commands, or device specific commands.
The IEEE-488.2 standard enhances and strengthens the IEEE-488.1 standard by specifying data formats, status reporting, error handling, controller functionality, and common instruments commands. It focuses mainly on the software protocol issues and thus maintains compatibility with the hardware- oriented IEEE-488.1 standard. IEEE-488.2 systems tend to be more compatible and reliable.
## Standards
The IEEE-488 standard is also know by a number of other names, which are either the same as the IEEE-488 standard, or are extentions to the original GPIB standard:
GPIB	General Purpose Interface Bus or General Purpose Instrumentation Bus
GPI Bus	Same as GPIB
GPIBA	GPIB Adapter
HPIB	Hewlett-Packard Interface Bus
IEEE-488	Adopted by the Institute of Electrical and Electronic Engineers (US Standard)
IEEE-488.2	Revision 2 of the IEEE-488 standard, specifying data formats, status reporting, error handling, controller functionality, and common instruments commands.
IEC 60488	Adopted by the International Electrotechnical Commission (International Standard)
IEC 60625-1	Adopted by the International Electrotechnical Commission (International Standard). This standard is replaced by IEC 60488.
IEC 60625-2	High-speed extentions to IEC 60625-1. This standard is replaced by IEC 60488.
IEEE-1174	An application of IEC 60625-2, which translates GPIB functionality to a serial RS232 line.
SCPI	built on the IEEE 488.2 standard and defines device-	specific commands that standardize programming	instruments
# Acorn's IEEE488 interface
## IEEE Interface
The Acorn IEEE Interface enables a British Broadcasting Corporation Microcomputer to control any scientific and technical equipment which conforms to the IEEE 488 standard.
Together, the IEEE Interface and BBC Microcomputer provide computer control of IEEE488-compatible devices at a lower price than other systems - but without sacrificing any aspect of the IEEE488 standard. And, as an added bonus, Interface users have available to them the full power and versatility of the BBC Microcomputer.
## Operation
The IEEE Interface is provided in its own case, designed to match the BBC Microcomputer. It can be linked to a network of up to 14 separate IEEE488-compatible devices: oscilloscopes, voltmeters, logic analysers, spectrum analysers, function generators, frequency meters, and any of the many other devices that are available.
When installed, the Interface automatically establishes the micro as the controlling device on the network. In addition, the micro can operate as a controller-talker or controller-listener and it can pass control to and from any other suitable device on the network. when not controlling the network the micro can operate as a talker or listener.
Typical applications of the Interface are in experimental work in academic and industrial laboratories. For example, the micro might be programmed to instruct one device to generate input signals at a range of frequencies, and to accept measurements of the corresponding output signals from a second device.
The advantages of computer-controlled operation over manual operation are speed, accuracy and repeatability. In addition, the data from the experiment are immediately available to the micro's analysis programs, giving almost instant results and allowing rapid comparison of the results of different tests.
Many other applications of the Interface exist in the monitoring and control of scientific and industrial processes.
## Control
Careful design of the Interface ensures that efficient hardware is matched by easy-to-use software.
A Read Only Memory plugging into one of the BBC Microcomputer's spare ROM slots provides the IEEE Interface Filing System (IEEEFS). This is a set of plain English commands which the programmer uses to pass instructions from the micro to the devices on the network. The micro regards the IEEEFS as another filing system like disc or tape, so that the format of the program statements which address the IEEEFS will already be familiar to those with experience of the BBC Microcomputer. In addition, the straightforward nature of the commands enables full control of an IEEE488 network to be achieved without a detailed understanding of the operation of the interface.
The IEEEFS commands can be incorporated into programs written in any of the high-level languages available on the BBC Microcomputer: BBC BASIC, 6502 Assembler and so on.
Commands are available for all the functions included in the IEEE488 standard, including both serial and parallel polling, timeouts, and enabling and disabling of local control for all or individual devices.
Full explanations of the IEEEFS commands, and examples of their use, are included in the User Guide supplied with the interface.
## Other facilities
The BBC Microcomputer/IEEE Interface combination provides more than just control of an IEEE network. When not being used with a network, or whilst two other devices on the network are communicating with each other, the usual range of facilities of the versatile BBC Microcomputer are available to the user.
Its renowned colour graphics capabilities provide the ideal way of presenting experimental results in an instantly understandable form. A second processor can be connected for even faster processing and greater memory capacity. Or the micro can be linked into Acorn's Econet local area network, making control of and data from the IEEE488 system available to all the other micros on the network.
The interface itself has an additional 1MHz bus connection, enabling it to be linked to any of the other interfaces which operate from this bus, such as Acorn's Teletext acquisition unit. Use of the IEEE Interface places no restrictions on the other applications of the BBC Microcomputer.
## The TMS9914A chip
The IEEE-488 interface uses Texas Instruments' TMS9914A controller chip to handle all data transfers to and from the IEEE-488 bus.
The following table gives a brief description of the TMS9914A's registers. Note that the A0 and A2 address lines are reversed in the IEEE-488 interface.
Address	Read	Write
&FC20	Interrupt Status 0	Interrupt Mask 0
&FC21	-	Address
&FC22	Address Status	-
&FC23	Command Pass Through	Parallel Poll
&FC24	Interrupt Status 1	Interrupt Mask 1
&FC25	-	Serial Poll
&FC26	Bus Status	Auxiliary Command
&FC27	Data In	Data Out

Please refer to the TMS9914A's datasheet for more detailed information.

# IEEE Filing Systems
## IEEEFS 0.2 (1983)
### Overview
## IEEEFS 0.5 (1983)
### Overview
The IEEE488 interface is a general purpose system for exchanging data between a number of devices in a local area. The control of transmission and reception of this information is handled by an IEEE filing system. This filing system behaves in the same way as other filing systems even though the source or destination of the filing system data may not be a data storage device.
The IEEE filing system differs from the filing system standard in the following respects:

OSFILE	not supported
OSARGS	only filing system identification supported
OSGBPB	not implemented
OSFIND	only input and output (up to 16 channels)
OSFSC	limited implementation

File handles given are in the range &F0 to &FF. File handle &FE and &FF are reserved for special use. Handle &FE is reserved for the DATA channel and handle &FF is reserved for the COMMAND channel. The remaining 14 channels are used as 'device' channels, which are used to send data to and receive data from a device.
OSWORD call with A=&80 is used to invoke IEEEFS commands from assembler.
The IEEEFS paged ROM claims 2 pages of absolute workspace and 1 page of private workspace

### Command summary
*IEEE

BBC DEVICE NO <addr>
CLEAR
DEVICE CLEAR
END OF STRING <string>
GO TO LOCAL <handle> (handle) EXECUTE
LISTEN <handle> (handle) EXECUTE
LOCAL LOCKOUT
PARALLEL POLL ENABLE <handle> <pp response>
PARALLEL POLL DISABLE <handle> (handle) EXECUTE
PARALLEL POLL REQUEST
PARALLEL POLL UNCONFIGURE
READ BINARY <no. of bytes>
REMOTE DISABLE
REMOTE ENABLE
REQUEST CONTROL
SELECTED DEVICE CLEAR <handle> (handle) EXECUTE
SERIAL POLL <handle> <count>
STATUS
TAKECONTROL <address>
TALK <handle>
TIMEOUT ON
TIMEOUT OFF
TRANSFER <no. of bytes>
TRIGGER <handle> (handle) EXECUTE
UNLISTEN
UNTALK
WRITE BINARY <no. of bytes>

### Operating system calls
#### OSFILE
Read or write a whole file or its attributes
Call address &FFDD
Indirect through &212 (FILEV)

OSFILE is not supported under IEEEFS 0.05. If OSFILE is called when IEEEFS 0.05 is active, it will return error &FE Bad command.

#### OSARGS
Read or write a file's attributes
Call address &FFDA
Indirect through &214 (ARGSV)

On entry:
A specifies action to be taken
X points to a 4 byte area in zero-page (always I/O processor)
Y contains file handle, or 0

A	X	Y	Action
0	d	0	A = &07 (IEEEFS's filing system number)
0	d	<>0	Error &FE : Bad Command
<>0	d	d	No action

d = don't care

On exit:
A is preserved, except when entering with A=0 and Y=0
X and Y are preserved
C, D, N, V and Z are undefined

When A=0 and Y=0, IEEEFS will return it's filing system number, which is 7.
When A=0 and Y contains a non-zero value, IEEEFS will return with error &FE Bad command.
When A<>0, no action will be taken and all registers are preserved

#### OSBGET
Read a single byte from an open file
Call address &FFD7
Indirect through &216 (BGETV)

On entry:
Y contains the file handle, as provided by OSFIND

On exit:
A contains the byte read
X and Y are preserved
C is set if (...), and indicates that the byte obtained is invalid
D, N, V and Z are undefined

IEEEFS's implementation of OSBGET only supports file handles &FE (the DATA channel) and &FF (the COMMAND channel). Any other file handle will return the error &DE Channel.
(incomplete!)

klad:
COMMAND channel: &0EFF moet 0 of &40 zijn, anders &06 Type mismatch
COMMAND channel: &0EFF = 0 en &0E24 = 0 then &0E24+=1 and exit (A=0)
COMMAND channel: &0EFF = 0 en &0E24 = 1 then &0E24+=1 and &0E24 = &0F00 and exit (A=&0F00)
COMMAND channel: &0EFF = 0 en &0E24 > 1 then A =&0F00,(?0E23) and &0E23-=1 and if &0E23 = 0 then &0E24 = 0 and exit else exit
COMMAND channel: &0EFF = &40 en &0E24 = 0 then &0E23=4 and &0E24+=1 and exit (A=&40)
COMMAND channel: &0EFF = &40 en &0E24 != 0 then A =&0EFF,(?0E23) and &0E23-=1 and if &0E23 = 0 then &0E24 = 0 and exit else exit
#### OSBPUT
Write a single byte to an open file
Call address &FFD4
Indirect through &218 (BPUTV)

On entry:
A contains the byte to be written
Y contains the file handle

On exit:
A, X and Y are preserved
C, D, N, V and Z are undefined

OSBPUT supports only file handles &FE (the DATA channel) and &FF (the COMMAND channel). Any other file handle will return the error &DE Channel.
(incomplete!)

#### OSGBPB
Read or write a group of bytes
Call address &FFD1
Indirect through &21A (GBPBV)

OSGBPB is not supported under IEEEFS 0.05. If OSGBPB is called when IEEEFS 0.05 is active, it will return error &FE Bad command.

#### OSFIND
Open or close a file for byte access
Call address &FFCE
Indirect through &21C (FINDV)

On entry:
A specifies action to be taken
X contains the LSB of the pointer to the filename
Y contains the MSB of the pointer to the filename

A	X	Y	Action
0	d	h	Close channel
<>0	LSB	MSB	Open channel

d = don't care
h = file handle

On exit:
A contains the file handle on opening, or 0 if no more file	handles were available. A is undefined when closing.
X and Y are undefined
C, D, N, V and Z are undefined

If A = 0 and Y = 0 then all channels will be closed, except the COMMAND and DATA channels
If A <> 0 then X and Y must point to a location where the filename is stored. The filename must be terminated by carriage return (&0D).
The filename contains one or two parameters with a value between 0 and 31. If two parameters are sent, the parameters must be seperated by a comma (&2C). No spaces are allowed between the parameters. IEEEFS will return the file handle in A, or if no more file handles were available, A will be 0.
When the filename starts with the string COMMAND, the COMMAND channel will be opened, and IEEEFS will return the COMMAND channel file handle (&FF) in A.
When the filename starts with the string DATA, the DATA channel will be opened, and IEEEFS will return the DATA channel file handle (&FE) in A.
COMMAND and DATA are not case-sensitive
The COMMAND and DATA strings can be abbreviated by means of a dot (&2E). If the COMMAND or DATA string is abbreviated without a dot, IEEEFS will return error &DC Syntax.

#### FSCV
Filing system control vector
No direct call address
Indirect through &21E (FSCV)

On entry:
A specifies action to be taken
X and Y contain relevant parameters (see table below)

A	X	Y	Action
6	d	d	New filing system start
7	d	d	Returns the file handle range
8	d	d	No action
other	d	d	Error &FE : Bad Command

d = don't care

When A=6 and Y=0, IEEEFS will (???). On exit, A=0, X will be preserved and Y=1.
When A=7, IEEEFS will return it's file handle range. On exit, A will be preserved, X contains the minimum file handle and Y contains the maximum file handle. In IEEEFS 0.2 the minimum value is &FE and the maximum value is &FF.
When A=8, IEEEFS will take no action. All registers will be preserved
All other actions will result in error &FE Bad command

#### OSWORD &80 (128)
Call address &FFF1
Indirect through &20C (WORDV)

On entry:
A=&80 (128)
X and Y contain the address of a parameter block

Parameter block on entry:

XY+	0 Points to the first byte available after the parameters on entry (e.g. n+1) / 1 Pointer to parameters requested (e.g. 3) / 2 Command / 3 Don't care / 4 Parameter 1 / : : / : / n : / Parameter n

On exit:
A=preserved (&80)
X and Y are preserved (address of the parameter block)

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Parameter 1 / : : / : / n : / Parameter n

Notes:
If OSWORD &80 is called with a command code that are not listed below, IEEEFS will return the error mesage &FE Bad command
Only commands &01 and &02 can be called with XY+0 set to 0. Any other command value in combination with XY+0 = 0 will result in &FE Bad command

#### Command &01 : STATUS
Parameter block on entry:

XY+	0 &03 / 1 &07 / 2 &01 / 3 Don't care / 4 Don't care / 5 Don't care / 6 Don't care

XY+0 must be 0, otherwise an 'Out of range' error message will be displayed
XY+1 must be 4, otherwise an 'Out of range' error message will be displayed

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Bit 0 : Timeout on output / Bit 1 : Timeout on input / Bit 2 : Computer is controller in charge / Bit 3 : TRANSFER in progress / Bit 4 : String of more than 255 characters received / Bit 5 : SRQ service remote message received / Bit 6 : END end remote message received / Bit 7 : Incomplete source handshake / 4 Bit 0 : Binary coded data being handled / Bit 1 : TIMEOUT on / Bit 2 : COMMAND handle is open / Bit 3 : DATA handle is open / Bit 4 : A device has been TALKed / Bit 5 : A device or devices have been LISTENed / Bit 6 : BBC DEVICE NO executed / Bit 7 : CLEAR executed / 5 Bit 0 : Input error / Bit 1 : Output error / Bit 2 : Conflict for control of interface / Bit 3 : Computer in process of becoming controller in charge / Bit 4 : Computer in process of acknowledging an unidentified command from another device / Bit 5 : Computer in process of entering the controller active state following a TRANSFER command / Bit 6 : unused / Bit 7 : REN remote enable remote message being sent / 6 Bit 0-6 : Unused / Bit 7 : Non-fatal error

On exit:
A, X and Y are preserved
C, D, N, V and Z are undefined

#### Command &02 : PARALLEL POLL REQUEST
Parameter block on entry:

XY+	0 &03 / 1 &04 / 2 &02 / 3 Don't care

XY+0 must be 0, otherwise an 'Out of range' error message will be displayed
XY+1 must be 1, otherwise an 'Out of range' error message will be displayed

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 TMS9914A's Command Passthrough Register

On exit:
A, X and Y are preserved
C, D, N, V and Z are undefined

#### Command &10 : TRANSFER
Parameter block on entry:

XY+	0 &07 / 1 &03 / 2 &01 / 3 / 4 / 5 / 6 LSB Number of bytes / : / : / MSB Number of bytes

XY+0 must be 4, otherwise an 'Out of range' error message will be displayed
XY+1 must be 0, otherwise an 'Out of range' error message will be displayed

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 / 4 / 5 / 6

On exit:
A, X and Y are preserved
C, D, N, V and Z are undefined

#### Command &14 : READ BINARY
Parameter block on entry:

XY+	0 &07 / 1 &03 / 2 &14 / 3 / 4 / 5 / 6 LSB Number of bytes / : / : / MSB Number of bytes

XY+0 must be 4, otherwise an 'Out of range' error message will be displayed
XY+1 must be 0, otherwise an 'Out of range' error message will be displayed

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 / 4 / 5 / 6

On exit:
A, X and Y are preserved
C, D, N, V and Z are undefined

#### Command &18 : WRITE BINARY
Parameter block on entry:

XY+	0 &07 / 1 &03 / 2 &18 / 3 / 4 / 5 / 6 LSB Number of bytes / : / : / MSB Number of bytes

XY+0 must be 4, otherwise an 'Out of range' error message will be displayed
XY+1 must be 0, otherwise an 'Out of range' error message will be displayed
Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 / 4 / 5 / 6

On exit:
A, X and Y are preserved
C, D, N, V and Z are undefined

#### Command &20-&3F, &60-&7F, &A0-&BF, &E0-&FF :
Parameter block on entry:

XY+	0 &04-&12 / 1 &03 / 2 &20-&3F, &60-&7F, &A0-&BF, &E0-&FF / 3 Parameter 1 / : : / : : / n Parameter n

This will cycle through all the parameters (channels) and send the one or two parameters which were given while opening the channel with the OSFIND call to the Data Out register using &9556

XY+0 must be between &04 and &12, otherwise an 'Out of range' error message will be displayed
XY+1 must be &03, otherwise an 'Out of range' error message will be displayed
If the command &20 is issued, first a call to &95DD will be made (some flags will be reset) at &87CE
All other commands will call &90B2 (OSWORD &80 command &54) first at &87D4
Parameters will be handled from last to first, e.g. from n to 2.
All parameters must be between &F0 and &FD (these are probably file handles). Now this will become interesting since XY+2 is also handled and this one can also contain other values than file handles.....
If a channel was not opened, an error &DE Channel will be printed

On exit:
A, X and Y are preserved
C, D, N, V and Z are undefined

#### Command &40 : BBC DEVICE NO
This will set the controller's GPIB address.
Parameter block on entry:

XY+	0 &04 / 1 &03 / 2 &40 / 3 Bit 0-4 : GPIB address / Bit 5-7 : Unused

This will replace the value of (&C8),0 with XY+3 and set bit 6 of (&C6),1

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Preserved

On exit:
A, X and Y are preserved
C, D, N, V and Z are undefined

Possible errors:

&88 Out of range	Check if XY+0 is &01, XY+1 is &00 and XY+3 is between &00 and &1F

#### Command &41 : TALK
Parameter block on entry:

XY+	0 &04 / 1 &03 / 2 &41 / 3 &F0-&FD (Channel)

This will send the one or two parameters which were given while opening the channel with the OSFIND call to the Data Out register using &957B

XY+0 must be 1, otherwise an 'Out of range' error message will be displayed
XY+1 must be 0, otherwise an 'Out of range' error message will be displayed
XY+3 must be between &F0 and &FD, otherwise an 'Out of range' error message will be displayed
If XY+3 was not opened, an error &DE Channel will be printed

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Preserved

On exit:
A, X and Y are preserved
C, D, N, V and Z are undefined

#### Command &42 : TAKE CONTROL
Parameter block on entry:

XY+	0 &04 / 1 &03 / 2 &42 / 3 &F0-&FD (Channel)

XY+0 must be 1, otherwise an 'Out of range' error message will be displayed
XY+1 must be 0, otherwise an 'Out of range' error message will be displayed
If XY+3 was not opened, an error &DE Channel will be printed

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Preserved

On exit:
A, X and Y are preserved
C, D, N, V and Z are undefined

#### Command &44 : SERIAL POLL
Parameter block on entry:

XY+	0 &05 / 1 <>0 / 2 &44 / 3

XY+0 must be &05, otherwise an 'Out of range' error message will be displayed
XY+1 must not be 0, otherwise an 'Out of range' error message will be displayed
If XY+3 was not opened, an error &DE Channel will be printed

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Preserved

On exit:
A, X and Y are preserved
C, D, N, V and Z are undefined
#### Command &48 : PARALLEL POLL ENABLE
Parameter block on entry:

XY+	0 &04 / 1 &03 / 2 &48 / 3 &F0-&FD (Channel) / 4 Bit 0-2 : Desired parallel poll response / Bit 3 : Sense bit / Bit 4-7 : Unused

This will send a PPC (Parallel Poll Configure) and a PPE (Parallel Poll Enable) command to the GBIP bus. The PPE command will be issued with the sense bit and desired parallel poll response given in XY+4.

XY+0 must be 2, otherwise an 'Out of range' error message will be displayed
XY+1 must be 0, otherwise an 'Out of range' error message will be displayed
XY+3 must be between &F0 and &FD, otherwise an 'Out of range' error message will be displayed
XY+4 must be between &00 and &0F, otherwise an 'Out of range' error message will be displayed
If XY+3 was not opened, an error &DE Channel will be printed

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Preserved / 4 Preserved

On exit:
A, X and Y are preserved
C, D, N, V and Z are undefined

#### Command &50 : CLEAR
This will issue a software reset of the IEEE488 controller.
Parameter block on entry:

XY+	0 &03 / 1 &03 / 2 &50

XY+0 must be 0, otherwise an 'Bad command' error message will be displayed
XY+1 must be 0, otherwise an 'Bad command' error message will be displayed
This will first check if an primary address has been assigned to the controller. If not , then error &8B (No BBC device no) will be generated.
1. Send the 'Set Software reset' mnemonic to the TMS9914A's Auxiliary command register
2. Set the SPAS, END and B0 bits in the Interrupt Mask 0 register, and clear all other bits
3. Set the SRQ and MA bits in the Interrupt Mask 1 register, and clear all other bits
4. Set the Address register to the primary address assigned using OSWORD &80 command &40
5. Send the 'Set Send interface clear' mnemonic to the Auxilliary command register
6. Clear all bits of (&C6),0
7. Clear bits 7, 5, 4 and 0 of (&C6),1
8. Clear all bits of (&C6),2
9. Clear all bits of (&C6),3
10. Send the 'Clear Software reset' mnemonic to the TMS9914A's Auxiliary command register
(...)

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved

On exit:
A, X and Y are preserved
C, D, N, V and Z are undefined

Possible errors:

&8B No BBC device no	No primary GPIB address has been assigned to the controller. Issue an OSWORD &80 command &40 first to specify the address

&FE Bad command	Check if XY+0 and XY+1are both set to &00

#### Command &51 : TIMEOUT ON
Parameter block on entry:

XY+	0 &03 / 1 &03 / 2 &51

This will set bit 1 of (&C6),1

XY+0 must be 0, otherwise an 'Bad command' error message will be displayed
XY+1 must be 0, otherwise an 'Bad command' error message will be displayed

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved

On exit:
A, X and Y are preserved
C, D, N, V and Z are undefined

#### Command &52 : TIMEOUT OFF
Parameter block on entry:

XY+	0 &03 / 1 &03 / 2 &52

This will clear bit 1 of (&C6),1

XY+0 must be 0, otherwise an 'Bad command' error message will be displayed
XY+1 must be 0, otherwise an 'Bad command' error message will be displayed

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved

On exit:
A, X and Y are preserved
C, D, N, V and Z are undefined

#### Command &54 : UNLISTEN
Parameter block on entry:

XY+	0 &03 / 1 &03 / 2 &54

This will send an UNL (Unlisten) command over the GPIB bus, and clear bit 5 of (&C6),1

XY+0 must be 0, otherwise an 'Bad command' error message will be displayed
XY+1 must be 0, otherwise an 'Bad command' error message will be displayed

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved

On exit:
A, X and Y are preserved
C, D, N, V and Z are undefined

#### Command &58 : UNTALK
Parameter block on entry:

XY+	0 &03 / 1 &03 / 2 &58

This will send an UNT (Untalk) command over the GPIB bus, and clear bit 4 of (&C6),1

XY+0 must be 0, otherwise an 'Bad command' error message will be displayed
XY+1 must be 0, otherwise an 'Bad command' error message will be displayed

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved

On exit:
A, X and Y are preserved
C, D, N, V and Z are undefined

#### Command &60 : PARALLEL POLL UNCONFIGURE
Parameter block on entry:

XY+	0 &03 / 1 &03 / 2 &60

This will send a PPU (Parallel Poll Unconfigure) command to the GPIB bus

XY+0 must be 0, otherwise an 'Bad command' error message will be displayed
XY+1 must be 0, otherwise an 'Bad command' error message will be displayed

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved

On exit:
A, X and Y are preserved
C, D, N, V and Z are undefined

#### Command &61 : LOCAL LOCKOUT
Parameter block on entry:

XY+	0 &03 / 1 &03 / 2 &61

This will send a LLO (Local Lockout) command to the GPIB bus.

XY+0 must be 0, otherwise an 'Bad command' error message will be displayed
XY+1 must be 0, otherwise an 'Bad command' error message will be displayed

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved

On exit:
A, X and Y are preserved
C, D, N, V and Z are undefined

#### Command &62 : DEVICE CLEAR
Parameter block on entry:

XY+	0 &03 / 1 &03 / 2 &62

This will send a DCL (Device Clear) command to the GPIB bus

XY+0 must be 0, otherwise an 'Bad command' error message will be displayed
XY+1 must be 0, otherwise an 'Bad command' error message will be displayed

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved

On exit:
A, X and Y are preserved
C, D, N, V and Z are undefined

#### Command &64 : REQUEST CONTROL
Parameter block on entry:

XY+	0 &03 / 1 &03 / 2 &64

This will set the rsv1 bit in the controller's Serial Poll register

XY+0 must be 0, otherwise an 'Bad command' error message will be displayed
XY+1 must be 0, otherwise an 'Bad command' error message will be displayed

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved

On exit:
A, X and Y are preserved
C, D, N, V and Z are undefined

#### Command &70 : REMOTE ENABLE
Parameter block on entry:

XY+	0 &03 / 1 &03 / 2 &70

This will send the 'Set sre' mnemonic to the TMS9914A's Auxiliary command register.

XY+0 must be 0, otherwise an 'Bad command' error message will be displayed
XY+1 must be 0, otherwise an 'Bad command' error message will be displayed

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved

On exit:
A, X and Y are preserved
C, D, N, V and Z are undefined

#### Command &71 : REMOTE DISABLE
Parameter block on entry:

XY+	0 &03 / 1 &03 / 2 &71

This will send the 'Clear sre' mnemonic to the TMS9914A's Auxiliary command register.

XY+0 must be 0, otherwise an 'Bad command' error message will be displayed
XY+1 must be 0, otherwise an 'Bad command' error message will be displayed

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved

On exit:
A, X and Y are preserved
C, D, N, V and Z are undefined

#### Command &81 : END OF STRING
Parameter block on entry:

XY+	0 &04 or &05 / 1 &03 / 2 &81 / 3 Second EOS byte / 4 First EOS byte

This will set the EOS character or characters.
XY+0 must be 0, 1 or 2, otherwise an 'String too long' error message will be displayed. The value 0 is probably a bug since it will point to the command code, and is never processed. The value 0 should probably return &88 Out of range (see &8838)
XY+1 must be 0, otherwise an 'Out of range' error message will be displayed
Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Preserved / 4 Preserved

On exit:
A, X and Y are preserved
C, D, N, V and Z are undefined

### Memory usage
#### &B0 - &BF : Filesystem's temporary workspace
&B0 - &B1	Pointer to private workspace (as reserved by ROM service call &02)

#### &C0 - &CF : Filesystem's private workspace
&C0 - &CF	Unused

### Error messages
#### Bad command (&FE)
The file system did not recognize the command, or the command was not called correctly
#### Channel (&DE)
An invalid file handle was used. The specified filehandle may already be closed, may not be opened successfully, or was not in the range between &F0 and &FF
#### Clear not executed (&8C)
bla bla bla
#### No BBC device no (&8B)
No primary GPIB address has been assigned to the controller. Issue an OSWORD &80 command &40 first to specify the address
#### No device listened (&8A)
bla bla bla
#### No device talked (&89)
bla bla bla
#### Out of range (&88)
bla bla bla
#### String too long (&8D)
The maximum length of a string is 255 characters
#### Syntax (&DC)
The maximum length of a string is 255 characters
#### Type mismatch (&06)
bla bla bla

osword klad:

C might be set after an OSWORD call, if it exits in ESCAPE mode ?

During a call:
&EF = A
&F0 = &BA = X
&F1 = &BB = Y
If XY+1 != 0 then XY+1 = XY+1 - 3
XY+0 = XY+0 - 3

## IEEEFS 0.02 (1986)
### Overview
The IEEEFS paged ROM claims no absolute workspace. If Hazel workspace is available (on ?? and ??), IEEEFS will claim one page of it. If Hazel isn't available, it will claim one page of private workspace.
### Operating system calls
#### OSWORD &80 (128)
Call address &FFF1
Indirect through &20C (WORDV)

On entry:
A=&80 (128)
X and Y contain the address of a parameter block

Parameter block on entry:

XY+	0 Points to the first byte available after the parameters on entry (e.g. n+1) / 1 Pointer to parameters requested (e.g. 3) / 2 Command / 3 Don't care / 4 Parameter 1 / : : / : / n : / Parameter n

On exit:
A=preserved (&80)
X and Y are preserved (address of the parameter block)
C, D, N, V and Z are preserved

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Parameter 1 / : : / : / n : / Parameter n

Notes:
If OSWORD &80 is called with a command code that are not listed below, IEEEFS will exit with all registers and flags preserved

#### Command &00 : Get status
This will return several status bytes and set (pwrkspc),&02 and (pwrkspc),&03 to &00

Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &00 / 3 Don't care / 4 Don't care / 5 Don't care / 6 Don't care / 7 Don't care / 8 Don't care / 9 Don't care / A Don't care / B Don't care / C Don't care / D Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Read mode flag / bit 0 : Single or multiple closing bytes flag / bit 1 : Use timer during data read flag / bit 2 : TUBE flag / 5 Write mode flag / bit 0 : Single or multiple closing bytes flag / bit 1 : Use timer during data write flag / bit 2 : TUBE flag / 6 / 7 TMS9914A's Bus Status Register / TMS9914A's Address Status Register / 8 APT/IFC interrupt flag. If bit 3 or 7 are set, then an an APT or IFC interrupt occurred since the last OSWORD &80 command &00 call. / Bit 0-2 : Unused / Bit 3 : APT interrupt flag / Bit 4-6 : Unused / Bit 7 : IFC interrupt flag / 9 (pwrkspc),&03 / A Bit 0-4 : GPIB address / Bit 5-6 : unused / Bit 7: ??? / B 'Active controller' flag / C (pwrkspc),&05 / D 'Allow interrupts' flag

XY+A	Bits 0-4 contain the controller's current GPIB address
Bits5-6 are unused
Bit 7 ???

XY+B	This byte is set to &FF if the IEEE488 controller is currently the active controller on the GPIB bus. If set to &00, the controller is not the active controller on the bus.
#### Command &01 : Set GPIB address
This will set (pwrkspc),&FE to XY+4

Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &01 / 3 Don't care / 4 Bit 0-4 : GPIB address / Bit 5-6 : unused / Bit 7 : ???

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved

#### Command &02 : Get GPIB address
This will return the value of (pwrkspc),&FE in XY+4

Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &02 / 3 Don't care / 4 Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Bit 0-4 : GPIB address / Bit 5-6 : unused / Bit 7 : ???

#### Command &03 : Set EOS (End Of String) characters during writes
This will set the EOS (End Of String) characters used when writing data to the IEEE488 bus. When a string is send, the end of this string can be signalled using hardware (EOI) or software (EOS). When using software, the string will be automatically terminated by the one or two characters defined using this command.
The character is usually LF when using one EOS. When using two EOS' the first character is usually CR, and the second LF.
See also OSWORD &80 command &04 and command &08.
Parameter block on entry:

XY+	0 &05 (one EOS character) or &06 (two EOS characters) / 1 Don't care / 2 &03 / 3 Don't care / 4 First EOS character / 5 Second EOS character

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved / 5 Preserved

#### Command &04 : Set EOS (End Of String) characters during reads
This will set the EOS (End Of String) characters used when reading data from the IEEE488 bus. When a string is received, the end of this string can be signalled using hardware (EOI) or software (EOS). When using software, the string will be automatically terminated by the one or two characters defined using this command.
The character is usually LF when using one EOS. When using two EOS' the first character is usually CR, and the second LF.
See also OSWORD &80 command &03 and command &08.
Parameter block on entry:

XY+	0 &05 (one EOS character) or &06 (two EOS characters) / 1 Don't care / 2 &03 / 3 Don't care / 4 First EOS character / 5 Second EOS character

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved / 5 Preserved

#### Command &05 : Set time-out timer
This command will substract the 32-bit value of XY+4 from zero (0) and store it in (pwrkspc),&FA till (pwrkspc),&FD
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 Command / 3 Don't care / 4 / 5 / 6 / 7 LSB / : / : / MSB

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 &05 / 3 Error code / 4 / 5 / 6 / 7 Preserved / : / : / Preserved

#### Command &06 : Use timer during data transfer
When this command is issued, the timer will be used during data transfers. The timer value can be set using OSWORD &80 command &05.
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &06 / 3 Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code

#### Command &07 : Do not use timer during data transfer
When this command is issued, no timer will be used during data transfers. Only the END, SPAS and SPAS/BO hardware time-outs will be used.
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &07 / 3 Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code

#### Command &08 : Set write mode
This will set the data transfer mode when writing to the IEEE488 bus.
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &08 / 3 Don't care / 4 Bit 0-1 : / 00: use EOS characters, don't send EOI with last byte, (...) / 01: don't use EOS characters, send EOI with last byte, (...) / 10: don't use EOS characters, send EOI with last byte, (...) / 11: use EOS characters, don't send EOI with last byte, (...) / Bit 2-7 : Unused

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved

#### Command &09 : Set read mode
This will set the data transfer mode when reading from the IEEE488 bus.
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &09 / 3 Don't care / 4 Bit 0-1 : / 00: use EOS characters, don't send EOI with last byte, (...) / 01: don't use EOS characters, send EOI with last byte, (...) / 10: don't use EOS characters, send EOI with last byte, (...) / 11: use EOS characters, don't send EOI with last byte, (...) / Bit 2-7 : Unused

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved

#### Command &0A : Reset
This will reset the IEEE488 controller and initialise the IEEEFS.
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &0A / 3 Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code

#### Command &0B : Set Send interface clear
This will send the Set Send interface clear mnemonic to the IEEE488 controller, and set the 'this controller is the active controller' flag.
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &0B / 3 Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code

Note: If (pwrkspc),&05 was set to &00, this call will exit with XY+3 set to &02

#### Command &0C : Clear Send interface clear
This will send the Clear Send interface clear mnemonic to the IEEE488 controller.
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &0C / 3 Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code

Note: If (pwrkspc),&05 was set to &00, this call will exit with XY+3 set to &02

#### Command &0D : Strobe Interface clear
This resets the GPIB bus by asserting the 'interface clear' (IFC) bus line for a duration of at least ??? microseconds. The interface clear causes all devices to untalk and unlisten, and puts them into serial poll disabled state (you will still be able to conduct serial polls). After releasing the IFC bus line the IEEE488 interface becomes the controller-in-charge.
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &0D / 3 Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code

Note: If (pwrkspc),&05 was set to &00, this call will exit with XY+3 set to &02

#### Command &0E : Set Send remote enable
This will send the Set Send remote enable mnemonic to the IEEE488 controller.
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &0E / 3 Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code

Note: If (pwrkspc),&05 was set to &00, this call will exit with XY+3 set to &02

#### Command &0F : Clear Send remote enable
This will send the Clear Send remote enable mnemonic to the IEEE488 controller.
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &0F / 3 Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code

Note: If (pwrkspc),&05 was set to &00, this call will exit with XY+3 set to &02

#### Command &10 : Reset
This will clear bit 7 from (pwrkspc),&FE, set bits 6-0 from (pwrkspc),&FE to bits 6-0 from XY+4, reset the IEEE488 controller and initialise the IEEEFS.
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &10 / 3 Don't care / 4 Bit 0-4: GPIB address / Bit 5-6: / Bit 7: unused

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved

#### Command &11 : Reset
This will set bit 7 from (pwrkspc),&FE, set bits 6-0 from (pwrkspc),&FE to bits 6-0 from XY+4, reset the IEEE488 controller and initialise the IEEEFS. Then it will send the Set Send remote enable mnemonic to the IEEE488 controller, and strobe the Set interface clear.
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &11 / 3 Don't care / 4 Bit 0-4: GPIB address / Bit 5-6: / Bit 7: unused

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved

#### Command &12 :
If the device is in the REM (Remote) state and the controller is either in the LPAS (Listener Primary Addressed) state or LLO (Local Lockout) state, the call will issue a 'clear tca' (Take Control Asynchronously) auxiliary command.
If the device is in the REM (Remote) state and the controller is NOT in the LPAS (Listener Primary Addressed) state or LLO (Local Lockout) state, the call will issue a 'clear tca' (Take Control Aynchronously) auxiliary command. Then, if the controller is NOT in the TPAS (Talker Primary Addressed) state, or the ATN line is low (true), the call will also issue a 'clear shdw' (Shadow Handshake) auxiliary command.
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &12 / 3 Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &13 :
If the device is in the REM (Remote) state and the controller is either in the LPAS (Listener Primary Addressed) state or LLO (Local Lockout) state, the call will issue a 'clear tca' (Take Control Asynchronously) auxiliary command.
If the device is in the REM (Remote) state and the controller is NOT in the LPAS (Listener Primary Addressed) state or LLO (Local Lockout) state, the call will issue a 'clear tcs' (Take Control Synchronously) auxiliary command. Then, if the controller is NOT in the TPAS (Talker Primary Addressed) state, or the ATN line is low (true), the call will also issue a 'clear shdw' (Shadow Handshake) auxiliary command.
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &13 / 3 Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &14 : Send addresses to IEEE488 bus
This will send parameter 1 to parameter n to the IEEE488 bus. If bit 5 of a parameter is set, bits 0-4 will be used to send a MLA (My Listen Address). If bit 6 of a parameter is set, bits 0-4 will be used to send a MTA (My Talk Address). Everything else will be send straight to the IEEE488 bus.
Parameter block on entry:

XY+	0 &05 or more / 1 Don't care / 2 &14 / 3 Don't care / 4 Parameter 1 / : : / : / n : / Parameter n

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved / : : / : / n : / Preserved

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &15 : MLA (My Listen Address)
This will send a MLA (My Listen Address) command using bits 0-4 of the address specified in XY+4 over the IEEE488 bus. Bits 5-7 of XY+4 are discarded.
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &15 / 3 Don't care / 4 Bit 0-4 : MLA GPIB address (&00 - &1F) / Bit 5-7 : Unused

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &16 : MLA (My Listen Address) and MSA (My Secondary Address)
This will send a MLA (My Listen Address) command using bits 0-4 of the address specified in XY+4 and a MSA (My Secondary Address) command using bits 0-4 of the address specified in XY+5 over the IEEE488 bus.Bits 5-7 of XY+4 and XY+5 are discarded.
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &16 / 3 Don't care / 4 Bit 0-4 : MLA GPIB address (&00 - &1F) / Bit 5-7 : Unused / 5 Bit 0-4 : MSA GPIB address (&00 - &1F) / Bit 5-7 : Unused

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved / 5 Preserved

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &17 : MTA (My Talk Address)
This will send a MTA (My Talk Address) command using bits 0-4 of the address specified in XY+4 over the IEEE488 bus. Bits 5-7 of XY+4 are discarded.
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &17 / 3 Don't care / 4 Bit 0-4 : MTA GPIB address (&00 - &1F) / Bit 5-7 : Unused

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &18 : MTA (My Talk Address) and MSA (My Secondary Address)
This will send a MTA (My Talk Address) command using bits 0-4 of the address specified in XY+4 and a MSA (My Secondary Address) command using bits 0-4 of the address specified in XY+5 over the IEEE488 bus. Bits 5-7 of XY+4 and XY+5 are discarded.
Parameter block on entry:

XY+	0 don't care / 1 don't care / 2 &18 / 3 don't care / 4 Bit 0-4 : MTA GPIB address (&00 - &1F) / Bit 5-7 : Unused / 5 Bit 0-4 : MSA GPIB address (&00 - &1F) / Bit 5-7 : Unused

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved / 5 Preserved

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &19 : MSA (My Secondary Address)
This will send a MSA (My Secondary Address) command using bits 0-4 of the address specified in XY+5 over the IEEE488 bus. Bits 5-7 of XY+4 are discarded.
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &19 / 3 Don't care / 4 Don't care / 5 Bit 0-4 : MSA GPIB address (&00 - &1F) / Bit 5-7 : Unused

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved / 5 Preserved

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &1A : UNL (Unlisten)
This will send an UNL (Unlisten) command over the IEEE488 bus
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &1A / 3 Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &1B : UNT (Untalk)
This will send an UNT (Untalk) command over the IEEE488 bus
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &1B / 3 Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &1C :
This will send an UNL (Unlisten) command, a MTA (My Talk Address) command with the controller's address specified with OSWORD &80 command &01, &10 or &11, a MLA (My Listen Address) command using bits 0-4 of the address specified in XY+4 and a GTS (Go To Standby) over the IEEE488 bus. Bits 5-7 of XY+4 are discarded.
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &1C / 3 Don't care / 4 Bit 0-4 : MLA GPIB address (&00 - &1F) / Bit 5-7 : Unused

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &1D :
This will send an UNL (Unlisten) command, a MTA (My Talk Address) command with the controller's address specified with OSWORD &80 command &01, &10 or &11, a MLA (My Listen Address) command using bits 0-4 of the address specified in XY+4, a MSA (My Secondary Address) command using bits 0-4 of the address specified in XY+5 and a GTS (Go To Standby) over the IEEE488 bus.Bits 5-7 of XY+4 and XY+5 are discarded.
Parameter block on entry:

XY+	0 don't care / 1 don't care / 2 &1D / 3 don't care / 4 Bit 0-4 : MLA GPIB address (&00 - &1F) / Bit 5-7 : Unused / 5 Bit 0-4 : MSA GPIB address (&00 - &1F) / Bit 5-7 : Unused

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved / 5 Preserved

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &1E :
This will send an UNL (Unlisten) command, a MLA (My Listen Address) command with the controller's address specified with OSWORD &80 command &01, &10 or &11, a MTA (My Talk Address) command using bits 0-4 of the address specified in XY+4 and a GTS (Go To Standby) over the IEEE488 bus. Bits 5-7 of XY+4 are discarded.
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &1E / 3 Don't care / 4 Bit 0-4 : MTA GPIB address (&00 - &1F) / Bit 5-7 : Unused

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &1F :
This will send an UNL (Unlisten) command, a MLA (My Listen Address) command with the controller's address specified with OSWORD &80 command &01, &10 or &11, a MTA (My Talk Address) command using bits 0-4 of the address specified in XY+4, a MSA (My Secondary Address) command using bits 0-4 of the address specified in XY+5 and a GTS (Go To Standby) over the IEEE488 bus.Bits 5-7 of XY+4 and XY+5 are discarded.
Parameter block on entry:

XY+	0 don't care / 1 don't care / 2 &1F / 3 don't care / 4 Bit 0-4 : MTA GPIB address (&00 - &1F) / Bit 5-7 : Unused / 5 Bit 0-4 : MSA GPIB address (&00 - &1F) / Bit 5-7 : Unused

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved / 5 Preserved

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &20 : Multiple GTL (Go To Local)
This will send an UNL (Unlisten) command, a MTA (My Talk Address) command with the controller's address specified with OSWORD &80 command &01, &10 or &11, cycle through all the parameters sending a MLA (My Listen Address) command using bits 0-4 of the parameter and send a GTL (Go To Local) over the IEEE488 bus. Bits 5-7 of parameters are discarded.
Parameter block on entry:

XY+	0 &05 or more / 1 Don't care / 2 &20 / 3 Not used / 4 Bit 0-4 : MLA GPIB address (&00 - &1F) / Bit 5-7 : Unused / : : / : / n : / Bit 0-4 : MLA GPIB address (&00 - &1F) / Bit 5-7 : Unused

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved / : : / : / n : / Preserved

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &21 : Multiple SDC (Selected Device Clear)
This will send an UNL (Unlisten) command, a MTA (My Talk Address) command with the controller's address specified with OSWORD &80 command &01, &10 or &11, cycle through all the parameters sending a MLA (My Listen Address) command using bits 0-4 of the parameter and send a SDC (Selected Device Clear) over the IEEE488 bus. Bits 5-7 of parameters are discarded.
Parameter block on entry:

XY+	0 &05 or more / 1 Don't care / 2 &21 / 3 Not used / 4 Bit 0-4 : MLA GPIB address (&00 - &1F) / Bit 5-7 : Unused / : : / : / n : / Bit 0-4 : MLA GPIB address (&00 - &1F) / Bit 5-7 : Unused

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved / : : / : / n : / Preserved

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &22 : Multiple GET (Group Execute Trigger)
This will send an UNL (Unlisten) command, a MTA (My Talk Address) command with the controller's address specified with OSWORD &80 command &01, &10 or &11, cycle through all the parameters sending a MLA (My Listen Address) command using bits 0-4 of the parameter and send a GET (Group Execute Trigger) over the IEEE488 bus. Bits 5-7 of parameters are discarded.
Parameter block on entry:

XY+	0 &05 or more / 1 Don't care / 2 &22 / 3 Don't care / 4 Bit 0-4 : MLA GPIB address (&00 - &1F) / Bit 5-7 : Unused / : : / : / n : / Bit 0-4 : MLA GPIB address (&00 - &1F) / Bit 5-7 : Unused

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved / : : / : / n : / Preserved

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &23 : LLO (Local Lockout)
This will send a LLO (Local Lockout) command over the IEEE488 bus
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &23 / 3 Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &24 : DCL (Device Clear)
This will send an DCL (Device Clear) command over the IEEE488 bus
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &24 / 3 Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &25 : PPU (Parallel Poll Unconfigure)
This will send an PPU (Parallel Poll Unconfigure) command over the IEEE488 bus
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &25 / 3 Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &26 : GTS (Go To Standby)
This will send an GTS (Go To Standby) command over the IEEE488 bus
If the device is in the REM (Remote) state and the controller is either in the LPAS (Listener Primary Addressed) state or LLO (Local Lockout) state, the call will issue a 'clear gts' (Go To Standby) auxiliary command.
If the device is in the REM (Remote) state and the controller is NOT in the LPAS (Listener Primary Addressed) state or LLO (Local Lockout) state, and the device is NOT in the LADS () state, or the ATN line is low (true), the call will also issue a 'set shdw' (Shadow Handshake) auxiliary command.
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &26 / 3 Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &27 : Set Serial Poll Register
This will send all bits except bit 6 of XY+4 to the IEEE488 controller's Serial Poll register. Bit 6 (the rsv1 bit, request service bit 1), will be set to 0.
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &27 / 3 Don't care / 4 Parameter

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved

#### Command &28 : RSV2 (Request Service Bit 2)
This will send the Set Request service bit 2 mnemonic to the IEEE488 controller.
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &28 / 3 Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code

Note: If the controller is set as the active controller on the IEEE488 bus, this function will return error code &04 in XY+3

#### Command &29 : Set Serial Poll Register with RSV2
This will send all bits except bit 6 of XY+4 to the IEEE488 controller's Serial Poll register. If bit 6 of XY+4 is set, it will also send the Set Request service bit 2 mnemonic to the IEEE488 controller.
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &29 / 3 Don't care / 4 Parameter

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved

Note: If the controller is set as the active controller on the IEEE488 bus, this function will return error code &04 in XY+3

#### Command &2A : Set UNC (Unrecognized Command) interrupt handler
This change the vector address of routine which is called when an interrupt occurs and the UNC flag is set in the controller's Interrupt Status Register 1.
The address specified in XY+4 and XY+5 must point to the address of the new handler minus 1. By default this handler points to &804D (so the handler is located at &804E), which does nothing.
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &2A / 3 Don't care / 4 / 5 LSB / MSB

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 / 5 Preserved / Preserved

#### Command &2B : SPE (Serial Poll Enable)
This will send an UNL (Unlisten) command, a MLA (My Listen Address) command with the controller's address specified with OSWORD &80 command &01, &10 or &11, a MTA (My Talk Address) command using bits 0-4 of the address specified in XY+4 and a GTS (Go To Standby) over the IEEE488 bus. Bits 5-7 of XY+4 are discarded.
It will then send a SPE (Serial Poll Enable) and a GTS (Go To Standby), read the Data In register, send SPD (Serial Poll Disable) and UNT (Untalk) over the IEEE488 bus.
The data read fron the Data In register is returned in XY+5
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &2B / 3 Don't care / 4 Bit 0-4 : MTA GPIB address (&00 - &1F) / Bit 5-7 : Unused / 5 Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved / 5 Data In register

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &2C : Get 'S-bit' bit
This will return the S-bit (the sense bit) of the last PPE (Parallel Poll Enable) command received. This S-bit will be matched against the ist-bit (the individual status of the instrument bit) during a PPE (Parallel Poll Enable) command. See chapter 3.7.1 of the TMS9914A's Data Manual for more information
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &2C

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Bit 0-2 : Unused / Bit 3 : S-bit / Bit 4-7 : Unused

#### Command &2D : Set 'ist' bit
This will set the 'individual status of the instrument' bit (represented by 'ist') used during a Parallel Poll. This 'ist' bit will be matched against the S-bit (the sense bit) during a PPE (Parallel Poll Enable) command. See chapter 3.7.1 of the TMS9914A's Data Manual for more information
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &2D / 3 Don't care / 4 Bit 0-2 : Unused / Bit 3 : ist-bit / Bit 4-7 : Unused

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved

#### Command &2E : PPE (Parallel Poll Enable)
This will send an UNL (Unlisten) command, a MLA (My Listen Address) command with the controller's address specified with OSWORD &80 command &01, &10 or &11, a MTA (My Talk Address) command using bits 0-4 of the address specified in XY+4 and a GTS (Go To Standby) over the IEEE488 bus. Bits 5-7 of XY+4 are discarded.

It will then send a PPC (Parallel Poll Configure), a PPE (Parallel Poll Enable) using bits 0-3 of XY+5 for its Parallel Poll Response and S-bit, and a UNL (Unlisten) over the IEEE488 bus.

Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &2E / 3 Don't care / 4 Bit 0-4 : MLA GPIB address (&00 - &1F) / Bit 5-7 : Unused / 5 Bit 0-2 : Parallel Poll Response / Bit 3 : S-bit (Sense Bit) / Bit 4-7 : Unused

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved / 5 Preserved

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &2F : PPD (Parallel Poll Disable)
This will send an UNL (Unlisten) command, a MLA (My Listen Address) command with the controller's address specified with OSWORD &80 command &01, &10 or &11, a MTA (My Talk Address) command using bits 0-4 of the address specified in XY+4 and a GTS (Go To Standby) over the IEEE488 bus. Bits 5-7 of XY+4 are discarded.

It will then send a PPC (Parallel Poll Configure) and a PPE (Parallel Poll Disable) over the IEEE488 bus.

Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &2F / 3 Don't care / 4 Bit 0-4 : MLA GPIB address (&00 - &1F) / Bit 5-7 : Unused

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &30 : Request Parallel Poll
This will send the parallel poll command over the interface. The status bits obtained from the Command Passthru register are returned in XY+4.

Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &30 / 3 Don't care / 4 Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Command Passthru Register

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &31 : SPD (Serial Poll Disable)
This will send an UNL (Unlisten) command, a MLA (My Listen Address) command with the controller's address specified with OSWORD &80 command &01, &10 or &11, a MTA (My Talk Address) command using bits 0-4 of the address specified in XY+4 and a GTS (Go To Standby) over the IEEE488 bus. Bits 5-7 of XY+4 are discarded.

It will then send a UNL (Unlisten) and a SPE (Serial Poll Disable) over the IEEE488 bus.

Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &31 / 3 Don't care / 4 Bit 0-4 : MTA GPIB address (&00 - &1F) / Bit 5-7 : Unused

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &32 : Set APT (Address Pass Through) interrupt handler
This change the vector address of routine which is called when an interrupt occurs and the APT flag is set in the controller's Interrupt Status Register 1.

The address specified in XY+4 and XY+5 must point to the address of the new handler minus 1. By default this handler points to &804D (so the handler is located at &804E), which does nothing.

Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &32 / 3 Don't care / 4 / 5 LSB / MSB

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 / 5 Preserved / Preserved

#### Command &33 : Set IFC (Interface Clear) interrupt handler
This change the vector address of routine which is called when an interrupt occurs and the IFC flag is set in the controller's Interrupt Status Register 1.

The address specified in XY+4 and XY+5 must point to the address of the new handler minus 1. By default this handler points to &804D (so the handler is located at &804E), which does nothing.

Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &33 / 3 Don't care / 4 / 5 LSB / MSB

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 / 5 Preserved / Preserved

#### Command &34 / &35 : Not implemented
These commands are not implemented and do nothing, except return error code &00 (Command executed sucessfully).

Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &34 / &35 / 3 Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code (always &00)

#### Command &36 : Write data to IEEE488
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &36 / 3 Don't care / 4 Don't care / 5 Don't care / 6 / 7 / 8 / 9 LSB Memory Address / : / : / MSB Memory Address / A / B / C / D LSB Number of bytes / : / MSB Number of bytes / Don't care / E / F / 10 / 11 Don't care / Don't care / Don't care / Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved / 5 Preserved / 6 / 7 / 8 / 9 Preserved / Preserved / Preserved / Preserved / A / B / C / D Preserved / Preserved / Preserved / Preserved / E / F / 10 / 11 LSB Number of bytes read / : / MSB Number of bytes read / &00

#### Command &37 : Read data from IEEE488
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &37 / 3 Don't care / 4 Don't care / 5 Don't care / 6 / 7 / 8 / 9 LSB Memory Address / : / : / MSB Memory Address / A / B / C / D LSB Number of bytes / : / MSB Number of bytes / Don't care / E / F / 10 / 11 Don't care / Don't care / Don't care / Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved / 5 Preserved / 6 / 7 / 8 / 9 Preserved / Preserved / Preserved / Preserved / A / B / C / D Preserved / Preserved / Preserved / Preserved / E / F / 10 / 11 LSB Number of bytes read / : / MSB Number of bytes read / &00

#### Command &38 : Write data to IEEE488
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &38 / 3 Don't care / 4 Bit 0-4 : MLA GPIB address (&00 - &1F) / Bit 5-7 : Unused / 5 Don't care / 6 / 7 / 8 / 9 LSB Memory Address / : / : / MSB Memory Address / A / B / C / D LSB Number of bytes / : / MSB Number of bytes / Don't care / E / F / 10 / 11 Don't care / Don't care / Don't care / Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved / 5 Preserved / 6 / 7 / 8 / 9 Preserved / Preserved / Preserved / Preserved / A / B / C / D Preserved / Preserved / Preserved / Preserved / E / F / 10 / 11 LSB Number of bytes read / : / MSB Number of bytes read / &00

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &39 : Read data from IEEE488
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &39 / 3 Don't care / 4 Bit 0-4 : MTA GPIB address (&00 - &1F) / Bit 5-7 : Unused / 5 Don't care / 6 / 7 / 8 / 9 LSB Memory Address / : / : / MSB Memory Address / A / B / C / D LSB Number of bytes / : / MSB Number of bytes / Don't care / E / F / 10 / 11 Don't care / Don't care / Don't care / Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved / 5 Preserved / 6 / 7 / 8 / 9 Preserved / Preserved / Preserved / Preserved / A / B / C / D Preserved / Preserved / Preserved / Preserved / E / F / 10 / 11 LSB Number of bytes read / : / MSB Number of bytes read / &00

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &3A : Write data to IEEE488
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &3A / 3 Don't care / 4 Bit 0-4 : MLA GPIB address (&00 - &1F) / Bit 5-7 : Unused / 5 Bit 0-4 : MSA GPIB address (&00 - &1F) / Bit 5-7 : Unused / 6 / 7 / 8 / 9 LSB Memory Address / : / : / MSB Memory Address / A / B / C / D LSB Number of bytes / : / MSB Number of bytes / Don't care / E / F / 10 / 11 Don't care / Don't care / Don't care / Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved / 5 Preserved / 6 / 7 / 8 / 9 Preserved / Preserved / Preserved / Preserved / A / B / C / D Preserved / Preserved / Preserved / Preserved / E / F / 10 / 11 LSB Number of bytes read / : / MSB Number of bytes read / &00

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &3B : Read data from IEEE488
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &3B / 3 Don't care / 4 Bit 0-4 : MTA GPIB address (&00 - &1F) / Bit 5-7 : Unused / 5 Bit 0-4 : MSA GPIB address (&00 - &1F) / Bit 5-7 : Unused / 6 / 7 / 8 / 9 LSB Memory Address / : / : / MSB Memory Address / A / B / C / D LSB Number of bytes / : / MSB Number of bytes / Don't care / E / F / 10 / 11 Don't care / Don't care / Don't care / Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved / 5 Preserved / 6 / 7 / 8 / 9 Preserved / Preserved / Preserved / Preserved / A / B / C / D Preserved / Preserved / Preserved / Preserved / E / F / 10 / 11 LSB Number of bytes read / : / MSB Number of bytes read / &00

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &3C : Write data to IEEE488
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &3C / 3 Don't care / 4 Bit 0-4 : MLA GPIB address (&00 - &1F) / Bit 5-7 : Unused / 5 Don't care / 6 / 7 / 8 / 9 LSB Memory Address / : / : / MSB Memory Address / A / B / C / D LSB Number of bytes / : / MSB Number of bytes / Don't care / E / F / 10 / 11 Don't care / Don't care / Don't care / Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved / 5 Preserved / 6 / 7 / 8 / 9 Preserved / Preserved / Preserved / Preserved / A / B / C / D Preserved / Preserved / Preserved / Preserved / E / F / 10 / 11 LSB Number of bytes read / : / MSB Number of bytes read / &00

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &3D : Read data from IEEE488
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &3D / 3 Don't care / 4 Bit 0-4 : MTA GPIB address (&00 - &1F) / Bit 5-7 : Unused / 5 Don't care / 6 / 7 / 8 / 9 LSB Memory Address / : / : / MSB Memory Address / A / B / C / D LSB Number of bytes / : / MSB Number of bytes / Don't care / E / F / 10 / 11 Don't care / Don't care / Don't care / Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved / 5 Preserved / 6 / 7 / 8 / 9 Preserved / Preserved / Preserved / Preserved / A / B / C / D Preserved / Preserved / Preserved / Preserved / E / F / 10 / 11 LSB Number of bytes read / : / MSB Number of bytes read / &00

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &3E : Write data to IEEE488
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &3E / 3 Don't care / 4 Bit 0-4 : MLA GPIB address (&00 - &1F) / Bit 5-7 : Unused / 5 Bit 0-4 : MSA GPIB address (&00 - &1F) / Bit 5-7 : Unused / 6 / 7 / 8 / 9 LSB Memory Address / : / : / MSB Memory Address / A / B / C / D LSB Number of bytes / : / MSB Number of bytes / Don't care / E / F / 10 / 11 Don't care / Don't care / Don't care / Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved / 5 Preserved / 6 / 7 / 8 / 9 Preserved / Preserved / Preserved / Preserved / A / B / C / D Preserved / Preserved / Preserved / Preserved / E / F / 10 / 11 LSB Number of bytes read / : / MSB Number of bytes read / &00

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

#### Command &3F : Read data from IEEE488
Parameter block on entry:

XY+	0 Don't care / 1 Don't care / 2 &3F / 3 Don't care / 4 Bit 0-4 : MTA GPIB address (&00 - &1F) / Bit 5-7 : Unused / 5 Bit 0-4 : MSA GPIB address (&00 - &1F) / Bit 5-7 : Unused / 6 / 7 / 8 / 9 LSB Memory Address / : / : / MSB Memory Address / A / B / C / D LSB Number of bytes / : / MSB Number of bytes / Don't care / E / F / 10 / 11 Don't care / Don't care / Don't care / Don't care

Parameter block on exit:

XY+	0 Preserved / 1 Preserved / 2 Preserved / 3 Error code / 4 Preserved / 5 Preserved / 6 / 7 / 8 / 9 Preserved / Preserved / Preserved / Preserved / A / B / C / D Preserved / Preserved / Preserved / Preserved / E / F / 10 / 11 LSB Number of bytes read / : / MSB Number of bytes read / &00

Note: If the controller is not set as the active controller on the IEEE488 bus, this function will return error code &03.

### Memory usage
#### File system's temporary workspace (zero page &B0-&BF)
&B0 - &B1	Pointer to private workspace (as reserved by ROM service call &02)
&B2 - &B5	32-bit pointer to memory location (used by OSWORD &80 commands &36 - &3F)
&B6 - &B8	24-bit number of bytes (used by OSWORD &80 commands &36 - &3F)
&B9	Interrupts flag. The interrupt routine uses this byte to signal normal code that certain interrupts have occurred. / Bit 0 : GET flag; a Group Execute Trigger interrupt has occurred / Bit 1 : Unused / Bit 2 : Unused / Bit 3 : Unused / Bit 4 : Unused / Bit 5 : Unused / Bit 6 : SRQ flag; a Service Request interrupt has occurred / Bit 7 : Interrupt flag; an GET or SRQ interrupt has occured
&BA - &BD	32-bit timer. Before each operation which requires the timer, &BA - &BD are set to the values of the private workspace page &FA - &FD
&BE - &BF

#### Filesystem's private workspace (zero page &C0-&CF)
&C0 - &CF	Unused

#### Filesystem's private workspace (as claimed by ROM service call &02)
Location	Description
&00	MTA (My Talk Address). This is the MTA for the controller. The address is the same as set by OSWORD &80 command &01. / bit 4-0: primary addresss for the TMS9914A / bit 5: set to 0 / bit 6: is set after setting the primary address at &86A7 / bit 7:set to 0
&01	MLA (My Listen Address). This is the MLA for the controller. The address is the same as set by OSWORD &80 command &01. / bit 4-0: primary addresss for the TMS9914A / bit 5: is set after setting the primary address at &86B0 / bit 6: set to 0 / bit 7: set to 0
&02	APT/IFC interrupt flag. If bit 3 or 7 are set, then an an APT or IFC interrupt occurred since the last OSWORD &80 command &00 call. OSWORD &80 command &00 call will reset this flag-byte to &00 / Bit 0-2 : Unused / Bit 3 : APT interrupt flag / Bit 4-6 : Unused / Bit 7 : IFC interrupt flag
&03
&04	'Allow interrupts' flag. It is used to signal the interrupt procedure that the private workspace has been set up, but that the controller hasn't been initialized yet. / &00: Private workspace has been initialized, but the controller hasn't / &FF: Private workspace has been initialized, and the controller has been reset using OSWORD &80 command &0A.
&05
&06	'Active controller' flag / &00: This controller is NOT the active controller on the GPIB bus / &FF: This controller IS the active controller on the GPIB bus
&07
&08	Parallel Poll response / bit 0-2: Parallel Poll Response / bit 3-7: unused (set to 0)
&09	Sense bit / bit 0-2: unused (set to 0) / bit 3 : S-bit of the last PPE command received / bit 4-7: unused (set to 0)
&0A	'TUBE claimed' flag / &00: TUBE not claimed by IEEEFS / &FF: TUBE claimed by IEEEFS
&0B - &EB	Unused
&EC
&ED	EOS character 1 used for writes (set by OSWORD &80 command &03)
&EE	EOS character 2 used for writes (set by OSWORD &80 command &03)
&EF - &F0	APT interrupt vector (see OSWORD &80 command &32)
&F1 - &F2	IFC interrupt vector (see OSWORD &80 command &33)
&F3 - &F4	UNC interrupt vector (see OSWORD &80 command &2A)
&F5	bit 0-2: unused (set to 0) / bit 3 : the individual status of the instrument bit (ist bit) as set by OSWORD &80 command &2D / bit 4-7: unused (set to 0)
&F6	Read mode
&F7	Write mode
&F8	EOS character 1 used for reads (set by OSWORD &80 command &03)
&F9	EOS character 2 used for reads (set by OSWORD &80 command &03)
&FA - &FD	32 bit timer; used for data transfer time-out's (set using OSWORD &80 command &05)
&FE
&FF

### Error codes
&00	Call completed successfully
&01
&02
&03	The call could not be executed because the controller wasn't the active controller on the IEEE-488 bus
&04	The call could not be executed because the controller was the active controller on the IEEE-488 bus
&05	A SRQ (Service Request) has been received during the call
&06	A GET (Group Execute Trigger) has been received during the call
&07	The call timed-out
&08	The specified length was 0 bytes

# Appendix A : IEEE488 connector pinout
The IEEE-488 interface system consists of 16 signal lines and 8 ground lines. The 16 signal lines are divided into 3 groups: 8 data lines, 3 handshake lines and 5 interface management lines.
Information is transmitted in a byte serial format by one talker to any number of listeners. Information consists of either data or commands. Eight data lines plus eight control lines (and eight ground lines) make up the bus. The pin assignments of these lines are given in Appendix A. Three of the control lines operate as a 3-wire handshake between talker (or controller) and listeners. No new data is sent until each device addressed to listen has received the previous byte and is ready for the next. This method of asynchronous communication ensures that the data rate is suited to the slowest active listener.
A standard 24-pin connector and cable is used. Instruments have female connectors and the cables have two male connectors. Cables also have each end of a second female connector. This permits stacking of cable connections at the connectors, somewhat like christmas tree light strings. Cables are typically six or nine feet each. AMP Incorporated, as well as many other firms sell prefabricated cables.

Figure 1 : IEEE488 connector

1	T	DIO1	13	T	DIO5
2	T	DIO2	14	T	DIO6
3	T	DIO3	15	T	DIO7
4	T	DIO4	16	T	DIO8
5	T/C	EOI	17	C	REN
6	C	DAV	18		Ground (DAV)
7	L	NRFD	19		Ground (NRFD)
8	L	NDAC	20		Ground (NDAC)
9	C	IFC	21		Ground (IFC)
10	T	SRQ	22		Ground (SRQ)
11	C	ATN	23		Ground (ATN)
12		Chassis ground	24		Single ground

DIO1 to DIO8	Data Input-Output bus; Bi-directional, Bite Serial-Byte Parallel. Per data line, bits are serial, ASCII data is sent as parallel data. Standard data is 7 bit ASCII. But no coding format is defined with IEEE-488.

EIO	End or Identify; Indicates the last data transfer of a multi-byte sequence or used by the system controller to indicate a Parallel Poll to a device (in conjunction with the ATN line).

DAV	Data Valid; Part of a three wire handshake. Used to indicate valid data on the bus, active low

NRFD	Not Ready For Data; Part of a three wire handshake. Used to indicate a device is ready for data, active low

NDAC	Not Data Accepted; Part of a three wire handshake. Used to indicate a device has not yet accepted data, active low

IFC	Interface Clear; Used only by the system controller to halt current operations. Placing all devices in an idle state. All talkers are set to Un-talk and all Listeners are set to Un-listen. Serial Poll is disabled. All devices shall monitor IFC, and respond within 100uS.

SRQ	Service Request; Used by any device to indicate that a device needs service. Any device may use this line. Normally used as an interrupt line. The controller may masked this line, in favor of Polling. The SRQ line is cleared by a Serial Poll

ATN	Attention; When low (true) the system places all devices in Command Mode, when high (false) the system places all devices in the Data Mode. In Command Mode the Controller passes data to devices, in Data Mode the Talker passes data to the Listener. All device must monitor the ATN line and respond within 200nS.

REN	Remote Enable; Used by the system controller to place devices in programming mode. All Remote capable Listeners are set to remote operation ( if they were addressed to Listen), when REN is true (low). When low, devices are set to Local control. All device shall monitor the REN line, and respond within 100uS.

# Appendix B: Parts list
Parts list
IC1	TMS9914ANL
IC2	SN75160AN
IC3	DS75162AN
IC4	SN74LS245N
IC5	SN74LS32N
IC6	??? (DIL14)
IC7	SN74LS32N
IC8	SN7404N
IC9	SN74LS04N
VR1	7805C

C1	10nF
C2	1000µF, 25V, radial
C3	220nF
C4	470nF
C5	100µF, 16V, radial
A1...A9	100nF

R1, R2	560 10%
R3	4k7 10%
RP1...RP4	2k2 resistor packs (DIL14)
DB1	G1 W005 8304

X1	5MHz

TR1	Drake Transformers C1206 prim.: 2x120v, sec.: 2x6v
FUSE	???
SW1	Power switch

S1, S2	3-pin jumper
PL1	Harting Connector 34H
PL2	power
PL3	Not fitted
SK1	24-pin AMP C24H IEEE488/GPIB connector
SK2	Harting Ribbon Cable Connector 4R34P

SHIELD	Solderpad/Testpad